| EEA/NSV/10/002 – ETC/ICM |  |
| --- | --- |

EEA 2012 report: Background document on thematic assessment on hydromorphology pressures

First draft

Version: 0.1

Date: July 12th 2011

EEA activity: 1.4.3

ETC/ICM task 1.4.3.e, milestone: 1

Prepared by / compiled by: János Fehér, János Maginecz, Judit Gáspár,

Kinga Szurdiné Veres

Organisation: VITUKI

EEA project manager: Peter Kristensen

Version history

| Version | Date | Author | Status and description | Distribution |
| --- | --- | --- | --- | --- |
| 0.1 | 12/07/2011 | JF | Pre-draft for ETC | circa |

Content

1.  Introduction of hydromorphological changes in European surface waters (rivers and lakes)	3

2.  Number of RBDs by countries for which data were available in the HYMO analysis	3

3  Datasets retrieved from RBMPs database	4

4  Characterization of surface water bodies	5

4.1 HMWBs and AWBs	5

Key messages on HMWBs and AWBs	7

Assessment on HMWBs and AWBs	7

4.2  HYMO pressures	7

Key messages on HYMO pressures	17

Conclusions	17

ANNEX 1	17

# 1.  Introduction of hydromorphological changes in European surface waters (rivers and lakes)

Europe’s surface freshwaters are affected by major modifications, such as water abstractions, water flow regulations (dams, weirs, sluices, and locks) and morphological alterations, straightening and canalisation, and disconnection of flood plains.

EU Member States have reported in 2010 via the River Basins Management Plans (RBMPs) the status and pressures related to hydromorphological pressures. Based on RBMPs and sector information (hydropower, inland water navigation and land use) an analysis is to be prepared and drafted an assessment on hydromorphological status and pressures.

This report aims to provide background materials for the preparation of the EEA’s 2012 Thematic assessment: Hydromorphological status and pressures.

Using the database on hydromorphological pressure and status data compiled from the submitted RBMPs under Task 1.4.3.e sets of maps and diagrams were produced providing overview of the status of hydromorphological pressures covering

- General characterisation, conceptual diagrams - regarding status and pressures -  for European water bodies illustrating: heavily modified water bodies, artificial water bodies,

- Water flow regulations and morphological alterations of surface water

- River management pressures

- Other morphological alteration

- Other pressures.

# 2.  Number of RBDs by countries for which data were available in the HYMO analysis

In the hydromorphological pressure analysis data from 180 RBDs of 13 countries were used.

(See detailed list of RBDs in Annex 1.)

Table 1 lists the countries and the number of RBDs per countries which were subject of analysis.  ETC ICM used data of those RBDs which were officially reported by Member States to EU COM via WFD reporting line.  In the first phase of the analysis data only from 71 RBDs of first nine countries were made available, and later 4 countries with additional 37 RBDs could be analysed.

Table 1.  Countries and the number of RBDs per countries involved in the analysis

| Country | Number of RBDs | Comment |
| --- | --- | --- |
| Austria | 3 |  |
| Bulgaria | 4 |  |
| Czech Republic | 3 |  |
| Finland | 8 | FIVVDA – there is no data for Aland RBD |
| France | 14 | FRM – there is no data for this RBD |
| Germany | 10 |  |
| The Netherlands | 4 |  |
| Sweden | 10 |  |
| UK | 15 |  |
| 9 countries | 71 |  |
| Greece | 14 |  |
| Lithuania | 4 |  |
| Slovakia | 2 |  |
| Spain | 17 | ES070 – Segura RBD no data for HMWB and AWB |
| 13 countries | 108 |  |

# 3  Datasets retrieved from RBMPs database

The following five groups of hydromorphological pressure information on surface waters (rivers and lakes) were included in the analysis from the RBDs.

3 Water abstractions

3.1 Agriculture

3.2 Public Water Supply

3.3 Manufacturing

3.4 Electricity cooling

3.5 Fish farms

3.6 Hydro-energy not cooling

3.7 Quarries

3.8 Navigation

3.9 Water transfer

3.10 Other

4 Water flow regulations and morphological alterations of surface water

4.1 Groundwater recharge

4.2 Hydroelectric dam

4.3 Water supply reservoir

4.4 Flood defence dams

4.5 Water Flow Regulation

4.6 Diversions

4.7 Locks

4.8 Weirs

5 River management

5.1 Physical alterations of channels

5.2 Engineering activities

5.6. Dredging

7 Other morphological alterations

7.1 Barriers

7.2 Land sealing

8 Other Pressures

8.2 Sludge disposal to sea

8.3 Exploitation/removal of animals/plants

8.6 Introduced species

8.10 Other

# 4  Characterization of surface water bodies

## 4.1 HMWBs and AWBs

WFD defines:  "Heavily modified water body" means a body of surface water which as a result of physical alterations by human activity is substantially changed in character, while "Artificial water body" means a body of surface water created by human activity.

Table 2 gives an overview on total number of river and lake water bodies reported in the RBMPs and the number of natural, heavily modified and artificial water bodies by countries.

Figure 1 and 2 gives an illustration on the number of different water body types and their percentage compared to the total number.

Figure 3 illustrates on map the ratio among the number of natural, heavily modified and artificial water bodies by countries using pie charts.

Table 2. Number of river and lake water body types by countries

| Country | RWB | LWB | Total SWB | Natural RWB | Natural LWB | HMWB R | HMWB L | Total HMWB | AWB R | AWB L | Total SW AWB |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AT | 7 339 | 62 | 7 401 | 6 674 | 37 | 570 | 6 | 576 | 95 | 19 | 114 |
| BG | 689 | 42 | 731 | 508 | 6 | 179 | 8 | 187 | 2 | 28 | 30 |
| CZ | 1 069 | 71 | 1 140 | 891 | 0 | 175 | 70 | 245 | 3 | 1 | 4 |
| FI | 1 602 | 4 261 | 5 863 | 1 519 | 4 204 | 79 | 32 | 111 | 4 | 25 | 29 |
| FR | 10 824 | 439 | 11 263 | 10 353 | 71 | 355 | 303 | 658 | 116 | 65 | 181 |
| DE | 9 074 | 712 | 9 786 | 4 235 | 509 | 3 485 | 92 | 3 577 | 1 354 | 111 | 1 465 |
| NL | 254 | 450 | 704 | 6 | 1 | 238 | 60 | 298 | 10 | 389 | 399 |
| SE | 15 563 | 7 232 | 22 795 | 15 183 | 6 984 | 368 | 247 | 615 | 12 | 1 | 13 |
| UK | 9 080 | 1 119 | 10 199 | 6 579 | 354 | 1 936 | 565 | 2 501 | 565 | 200 | 765 |
| GR | 1 033 | 29 | 1 062 | 913 | 20 | 95 | 9 | 104 | 25 | 0 | 25 |
| LT | 832 | 345 | 1 177 | 724 | 291 | 103 | 54 | 157 | 5 | 0 | 1 |
| SK | 1 760 | 0 | 1 760 | 1 700 | 0 | 53 | 0 | 53 | 7 | 0 | 7 |
| ES | 4 324 | 328 | 4 652 | 3 567 | 220 | 739 | 59 | 798 | 18 | 49 | 67 |

Figure 1. Number of River WB types (natural, HMWB and AWB) by countries

Figure 2.  % of River WB types (natural, HMWB and AWB) by countries

Figure 3. Ratio of River WB types (natural, HMWB and AWB) by countries

### Key messages on HMWBs and AWBs

-  There is a wide range of differences in the designated number of water bodies among the countries investigated (254 RWBs in NL and 15 563 RWBs in SE while in case of lakes SK has not identified any lake water bodies compared with 7232 LWBs of SE).

- In NL majority of the river water bodies are heavily modified while in SE almost all river water bodies are in natural condition.

- There is observable correlation between the higher percentage of HMWBs and AWBs and the level of population density.

### Assessment on HMWBs and AWBs

The number of countries for which data from RBMPs were available for analysis is not representative enough to draw overall conclusions on HMWB and AWB status at European level.  Out of 27 countries which were due to submit their RBMPs there were 9 countries which provided full sets of official data and four countries with still not fully official status data that could be included into the analysis until the time of report writing.

## 4.2  HYMO pressures

Five groups of hydromorphological pressure on surface waters (rivers and lakes) were included in the analysis, namely (1) Water abstractions; (2) Water flow regulations and morphological alterations of surface water; (3) River management; (4) Other morphological alterations; (5) Other pressures.  (Sub-categories are listed in Chapter 2.1 Datasets retrieved from RBMPs database.)

Two types of queries had been carried out both for river and lake water bodies.

First: all pressures were accounted by pressures groups. (See Table 3 and Table 4 for rivers and lakes, respectively and the related figures.)

Table 3.  Number of pressures on river water bodies by pressure categories

| Country | Total # of RWBs | 3. Water abstraction | 4. Water flow regulation and morphological alterations | 5. River management | 7. Other morphological alterations | 8. Other pressures |
| --- | --- | --- | --- | --- | --- | --- |
| AT | 7 339 | 40 | 4 105 | 0 | 212 | 0 |
| BG | 689 | 149 | 87 | 72 | 20 | 51 |
| CZ | 1 069 | 0 | 704 | 229 | 0 | 128 |
| FI | 1 602 | 3 | 125 | 180 | 55 | 148 |
| FR | 10 824 | 2 223 | 2 798 | 3 134 | 0 | 254 |
| DE | 9 074 | 182 | 7 744 | 0 | 0 | 548 |
| NL | 254 | 33 | 174 | 230 | 219 | 231 |
| SE | 15 563 | 73 | 4 561 | 4 120 | 0 | 526 |
| UK | 9 080 | 1 307 | 4 099 | 2 680 | 0 | 1 599 |
| GR | 1 033 | 62 | 0 | 1 | 0 | 0 |
| LT | 832 | 2 | 28 | 195 | 0 | 18 |
| SK | 1 760 | 0 | 0 | 0 | 0 | 0 |
| ES | 4 324 | 1 245 | 929 | 558 | 17 | 791 |
| BE |  | 12 | 139 | 0 | 0 | 49 |

Table 4.  Number of pressures on lake water bodies by pressure categories

| Country | Total # of RWBs | 3. Water abstraction | 4. Water flow regulation and morphological alterations | 5. River management | 7. Other morphological alterations | 8. Other pressures |
| --- | --- | --- | --- | --- | --- | --- |
| AT | 62 | 0 | 9 | 0 | 0 | 0 |
| BG | 42 | 8 | 0 | 0 | 0 | 8 |
| CZ | 71 | 0 | 62 | 5 | 0 | 36 |
| FI | 4 261 | 0 | 69 | 17 | 20 | 198 |
| FR | 439 | 47 | 79 | 2 | 8 | 7 |
| DE | 712 | 1 | 66 | 0 | 0 | 26 |
| NL | 450 | 87 | 229 | 296 | 276 | 332 |
| SE | 7 232 | 5 | 2 180 | 0 | 0 | 238 |
| UK | 1 119 | 176 | 790 | 642 | 0 | 173 |
| GR | 29 | 8 | 0 | 0 | 0 | 0 |
| LT | 345 | 4 | 0 | 0 | 0 | 43 |
| SK | 0 | 0 | 0 | 0 | 0 | 0 |
| ES | 328 | 15 | 26 | 0 | 0 | 77 |
| BE |  | 1 | 18 | 0 | 0 | 3 |

Figure 4.  Ratios of different HYMO pressures on river water bodies by countries

Figure 5.  Ratios of different HYMO pressures on river water bodies by RBDs

Figure 6.  Ratios of different HYMO pressures on lake water bodies by countries

Second:  the number of HYMO pressure affected water bodies was accounted.  A water body was considered affected if at least one HYMO pressure occurs on it. (See Table 5 and Table 6 for rivers and lakes, respectively and the related figures.)  Besides the total number of HYMO pressure affected RWBs, the number of HYMO pressure affected natural, heavily modified and artificial river water bodies were also accounted.

Table 5.  Number of RWBs with at least HYMO pressure

| Country | Total No. of RWB | No. of RWBs with HYMO pressure | No. of RWBs without HYMO pressure | Natural RWBs with HYMO pressures | Artificial RWBs with HYMO pressures | Heavily Modified RWBs with HYMO pressures |
| --- | --- | --- | --- | --- | --- | --- |
| AT | 7 339 | 4344 | 2 995 | 3701 | 73 | 570 |
| BE | 354 | 145 | 209 | 16 | 34 | 95 |
| BG | 689 | 284 | 405 | 189 | 0 | 95 |
| CZ | 1 069 | 867 | 202 | 691 | 2 | 174 |
| DE | 9 074 | 7832 | 1 242 | 3360 | 1121 | 3351 |
| ES | 4 324 | 1289 | 3 035 | 1001 | 1 | 287 |
| FI | 1 602 | 307 | 1 295 | 245 | 3 | 59 |
| FR | 10 824 | 5406 | 5 418 | 5069 | 38 | 300 |
| GR | 1 033 | 63 | 970 | 45 | 4 | 14 |
| LT | 832 | 239 | 593 | 236 | 0 | 3 |
| NL | 254 | 249 | 5 | 6 | 10 | 233 |
| SE | 15 563 | 7119 | 8 444 | 6755 | 9 | 355 |
| SK | 1 760 | 0 | 1 760 | 0 | 0 | 0 |
| UK | 9 080 | 5188 | 3 892 | 3026 | 271 | 1891 |

Table 6.  Number of LWBs with at least one HYMO pressure

| Country | Total No. of LWB | No. of LWBs with HYMO pressure | No. of LWBs with no HYMO pressure | Natural LWBs with HYMO pressures | Artificial LWBs with HYMO pressures | Heavily Modified LWBs with HYMO pressures | Unknown |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AT | 62 | 53 | 9 | 0 | 7 | 2 |  |
| BE | 18 | 0 | 18 | 0 | 13 | 5 |  |
| BG | 42 | 28 | 14 | 0 | 13 | 1 |  |
| CZ | 71 | 2 | 69 | 0 | 29 | 40 |  |
| DE | 712 | 629 | 83 | 17 | 23 | 43 |  |
| ES | 328 | 245 | 83 | 71 | 7 | 5 |  |
| FI | 4 261 | 4011 | 250 | 208 | 17 | 23 | 2 |
| FR | 439 | 310 | 129 | 68 | 40 | 21 |  |
| GR | 29 | 21 | 8 | 0 | 7 | 1 |  |
| LT | 345 | 298 | 47 | 31 | 4 | 12 |  |
| NL | 450 | 24 | 426 | 6 | 362 | 58 |  |
| SE | 7 232 | 4877 | 2355 | 1400 | 166 | 789 |  |
| SK | 0 | 0 | 0 | 0 | 0 | 0 |  |
| UK | 1 119 | 290 | 829 | 191 | 172 | 466 |  |

Figure 7.  Ratios of number of RWB types with at least one HYMO pressure by countries

Figure 8.  Ratios of number of RWB types with at least one HYMO pressure by RBDs

Figure 9.  Ratios of number of LWB types with at least one HYMO pressure by countries

Figure 10.  Ratios of number of LWB types with at least one HYMO pressure by RBDs

### Key messages on HYMO pressures

-  Water abstraction and water flow regulation and river management are significant pressures on rivers in high GDP countries (AT, FR, DE, SE and UK).

- Water abstraction causes relatively lower  pressure on river water bodies in drought and scarcity effected countries (GR, BG, and in partly in ES).

- HYMO pressure in some lower income (GDP) countries is relatively low on rivers and lakes (BG, GR, and LT)

-  No HYMO pressure was reported on any RWBs and no LWB was designated in SK.

-  85% of HYMO pressure effected RWBs in AT have natural WB status.

-  About 30% of HYMO pressure effected LWBs in SE have natural LWB status.

# Conclusions

When queries not only on main five pressure groups but on their sub-categories were carried out no consistency in country reporting on number of hydromorphological pressures (HYMO) on river and lake WBs was found.  (See 2nd Revised Working document - HYMO data- maps - graphs samples 20052011.doc uploaded to circa.)

Some countries (AT, GE, NL, UK, and SK) reported only about main groups of HYMO pressure (3. Water abstraction; 4. Water flow regulation and morphological alterations;  5. River management; 7. Other morphological alterations;  8. Other pressures) without giving details of such pressure groups.  Thus overall analysis on water level regulation in lakes or flow regulation could be done by selected RDBs or by countries in the next phase of the assessment.

Other countries reported HYMO pressures about the main groups and sub-groups as well, but the sum of sub-group numbers does not equal with the reported number of the main group.

Impacts and pressures relationships could be assessed in the function of WB types and main pressure groups and not in sub-pressure group types.

# ANNEX 1

Investigated river basins

| Country | EURBDCode | RBDName |
| --- | --- | --- |
| Austria | AT1000 | Danube |
|  | AT2000 | Rhine |
|  | AT5000 | Elbe |
| Bulgaria | BG1000 | Danube |
|  | BG2000 | BlackSea |
|  | BG3000 | East Aegean River |
|  | BG4000 | West Aegean River |
| Czech Rep. | CZ1000 | Danube |
|  | CZ2000 | Elbe |
|  | CZ6000 | Oder |
| Finland | FIVHA1 | Vuoksi |
|  | FIVHA2 | Kymjoki-Gulf of Finland |
|  | FIVHA3 | Kokemäenjoki-Archipelago Sea –Bothian Sea |
|  | FIVHA4 | Oulujoki-Iijoki |
|  | FIVHA5 | Kemijoki |
|  | FIVHA6 | Tornionjoki |
|  | FIVHA7 | Teno, Näätämöjoki and Paatsjoki |
|  | FIWDA | Åland |
| France | FRA | L'Escaut, la Somme et les cours d'eau côtiers de la Manche et de la mer du Nord |
|  | FRB1 | Meuse |
|  | FRB2 | La Sambre |
|  | FRC | Rhine |
|  | FRD | Le Rhône et les cours d'eau côtiers méditerranéens |
|  | FRE | Les cours d'eau de la Corse |
|  | FRF | L'Adour, la Garonne, la Dordogne, la Charente et les cours d'eau côtiers charentais et aquitains |
|  | FRG | La Loire, les cours d'eau côtiers vendéens et bretons |
|  | FRH | La Seine et les cours d'eau côtiers normands |
|  | FRI | Les cours d'eau de la Guadeloupe |
|  | FRJ | Les cours d'eau de la Martinique |
|  | FRK | Les fleuves et cours d'eau côtiers de la Guyane |
|  | FRL | Les cours d'eau de la Réunion |
|  | FRM | Les cours d'eau de Mayotte |
| Germany | DE1000 | Danube |
|  | DE2000 | Rhine |
|  | DE3000 | Ems |
|  | DE4000 | Weser |
|  | DE5000 | Elbe |
|  | DE6000 | Oder |
|  | DE7000 | Maas |
|  | DE9500 | Eider |
|  | DE9610 | Schlei/Trave |
|  | DE9650 | Warnow/Peene |
| Netherlands | NLEM | Ems |
|  | NLMS | Meuse |
|  | NLRN | Rhine |
|  | NLSC | Scheldt |
| Sweden | SE1 | 1.Bothnian Bay (Sweden) |
|  | SE1TO | Bothnian Bay (International district Torne river - Sweden) |
|  | SE2 | 2. Bothnian Sea (Sweden) |
|  | SE3 | North Baltic Sea (Sweden) |
|  | SE4 | South Baltic Sea (Sweden) |
|  | SE5 | Skagerrak and Kattegat (Sweden) |
|  | SENO1102 | 2. Bothnian Sea (International drainage basin Trondelagsfylkene - Sweden) |
|  | SENO1103 | 1. Bothnian Bay (International drainage basin Nordland - Sweden) |
|  | SENO1104 | 1. Bothnian Bay (International drainage basin Troms - Sweden) |
|  | SENO5101 | 5. Skagerrak and Kattegat (International drainage basin Glomma - Sweden) |
| UK | UK01 | Scotland |
|  | UK02 | Solway Tweed |
|  | UK03 | Northumbria |
|  | UK04 | Humber |
|  | UK05 | Anglian |
|  | UK06 | Thames |
|  | UK07 | SE |
|  | UK08 | SW |
|  | UK09 | Severn |
|  | UK10 | Western Wales |
|  | UK11 | Dee |
|  | UK12 | NW |
|  | UKGBNIIENB | Neagh Bann |
|  | UKGBNIIENW | North Western |
|  | UKGBNINE | North Eastern |
| Greece | GR01 | Western Peloponnese |
|  | GR02 | Northern Peloponnese |
|  | GR03 | Eastern Peloponnese |
|  | GR04 | Western Sterea Ellada |
|  | GR05 | Epirus |
|  | GR06 | Attica |
|  | GR07 | Eastern Sterea Ellada |
|  | GR08 | Thessalia |
|  | GR09 | Western Macedonia |
|  | GR10 | Central Macedonia |
|  | GR11 | Eastern Macedonia |
|  | GR12 | Thrace |
|  | GR13 | Crete |
|  | GR14 | Aegean Islands |
| Lithuania | LT1100 | Nemunas River Basin District |
|  | LT2300 | Venta River Basin District |
|  | LT3400 | Lielupe River Basin District |
|  | LT4500 | Dauguva River Basin District |
| Slovakia | SK30000 | Vistula |
|  | SK40000 | Danube |
| Spain | ES010 | Minho |
|  | ES014 | Galician coast |
|  | ES015 | Basque county internal basins |
|  | ES016 | Cantabrian |
|  | ES020 | Duero |
|  | ES030 | Tagus |
|  | ES040 | Guadiana RBD |
|  | ES050 | Guadalquivir |
|  | ES060 | Andalusia Mediterranean basins |
|  | ES063 | Guadalete and Barbate |
|  | ES064 | Tinto, Odiel and Piedras |
|  | ES070 | Segura |
|  | ES080 | Jucar |
|  | ES091 | Ebro |
|  | ES100 | Catalan RBD |
|  | ES110 | Balearic Islands |