|  | EEA | Matching monitoring stations – BE (FL) comments |
| --- | --- | --- |
|  | p/a VMM, A. Van de Maelestraat 96, B-9320 Erembodegem |
|  | Subject | Matching monitoring stations surface and ground waters - Flemish comments |
|  | Meeting date & Venue | 091020-21 EEA, Copenhagen / Thematic Freshwater Eionet Workshop on SOER and WISE assessments |
|  | Contacts | Flemish Environment Agency (VMM): Rudy Vannevel (SW, r.vannevel@vmm.be), Alistair Fronhoffs (GW, a.fronhoffs@vmm.be) |
|  | Copy to | Vincent Brahy ( Vincent.BRAHY@spw.wallonie.be), Jan Voet (j.voet@vmm.be) |

1) General comments

This initiative is very much appreciated as it is an important step towards an effective communication allowing common understanding of what is required, expected to be provided, available or has been reported in the past. The analysis is considered as being the first step in a process of systematic data analysis at EEA and EU level in order to obtain coherence in and between the datasets. This will facilitate discussions on the results at a later stage. The discussion during the meeting made clear that more detailed analyses from both sides will be necessary. Maybe this will require some bilateral meetings.

Because of the Belgian federal structure, the different water-related themes (surface water, ground water, TCM) as well as the long history of reporting, it is not always easy to get an overview of the data flows and the data reported to the international level. This explains some of the inconsistencies between sets of monitoring stations. In this respect we want to stress that it is important to agree on the sets of monitoring stations for the purpose of assessments, but also on the extend the data of matching stations will or can be used for other assessments. This requires that data treatment - the process between data and information (including data selection, algorithms, etc) – is transparent.

To facilitate communication and following the discussion of the meeting, it will be very much appreciated if we could dispose of the lists of monitoring stations available at EEA.

2) Ground water monitoring stations

Matching WISE-SoE, NiD and WFD art. 8 stations

Belgium – Flanders

Groundwater

The aim of this document is to explain the difference in groundwater stations reported in WISE-SoE, NiD and WFD art. 8 reports.

NiD : The monitoring stations for the Nitrate Directive are all located in agricultural areas. This phreatic groundwater network consists of about 2100 sites. These sites (wells) each usually have three separate filters installed at varying depths. The filters are installed in function of the redox conditions of the soil, the top filter is located near the groundwater surface, the second filter just above the reduction horizon and the third filter just below the reduction horizon (where nitrate cannot be present). For the Nitrate Directive the basic evaluation unit is the Hydrogeological Homogeneous Zone. Thirty-three Hydrogeological Homogeneous Zones were identified for Flanders. Within each of these zones there is an equal potential risk for nitrate contamination (based on hydrogeological characteristics). Thus, the basic evaluation unit system is a 2D-model, only applicable for the shallowest aquifers.

Within this evaluation framework every single site is reported separately but the different filters of a site are aggregated, leading to about 2100 reported sites.

WISE-SoE and WFD art. 8 : The main difference between WISE-SoE / WFD art. 8 and the NiD is the evaluation unit. For WISE SoE and WFD art. 8 the evaluation units are the groundwater bodies, which are delimited in 3D, based on general hydrogeological and stratigraphical characteristics of the aquifers. As explained above, the NiD units are delimited in 2D and are specifically created for nitrate monitoring (although it can also be used in a broader sense for diffuse contamination).

WISE-SoE : Aggregated data per groundwater body are delivered based on groundwater monitoring station of the phreatic groundwater network (as for the NiD) supplemented with phreatic monitoring stations in nature area. The aggregation of individual sites per groundwater body, and the overlying character of the groundwater bodies, means that one monitoring site, consisting of several filters at varying depths, can deliver information for one or more groundwater bodies (e.g. one site with 3 filters where filter 1 is situated in GWB X and filters 2 and 3 are situated, deeper, in GWB Y will give : 1 site in GWB X and 1 site in GWB Y).

WFD art. 8 : 42 virtual monitoring site are reported for WFD art. 8. Every groundwater body has one virtual monitoring point, with a number of subsites. In the future, other virtual groundwater monitoring points can be created to better differentiate the quality and quantity of the groundwater from agricultural areas, nature areas and drinking water protected areas.

3) Surface water monitoring stations

Matching WISE-SoE, NiD and WFD art. 8 stations

Belgium – Flanders

Surface water

To view the Flemish presentation of the meeting, please click

The presentation contains a grid table representing the number of monitoring stations of the WFD, WISE SoE and Nitrate Directive, as well as the number of overlap between sets (pair comparison). The table reveals that the WISE SoE can be considered as a complete subset of WFD, which allows a complete analysis of this subset based on WFD and WISE SoE data. However, similarity between WFD and NiDir monitoring stations is very low. For the purpose of the NiDir requirements and the Flemish action plans, this resulted in a large number of stations located on local water bodies.

Regarding the matching of monitoring stations at national level, as prepared and presented by ETC-W, it is important to stress that regional differences reflect mainly differences in geography, resulting in different land use, pressures and hence also policy and the number of monitoring stations.

A detailed analyses of monitoring stations (sets) is needed, based on a comparison of lists of stations.