Informal information and discussion document for the Joint SOE Drafting Group and Eionet Workshop

13 - 14 November 2006

1.	Estimation of ability of the present number of Eionet-water stations to determine national mean concentrations of different determinands

Eionet water is designed to obtain representative information on water quality in water bodies at the national level. Trends with time at the station level and national level are determined, and the most recent concentrations are ‘classified’ against class defining concentrations.

Two approaches are possible:

- Calculating the number of stations that would be needed (theoretically) to estimate the national station mean concentrations of determinands with specified degrees of precision and confidence.

- Calculating the precision in estimating the national station mean concentrations of determinands with specified levels of confidence based on the actual number of stations reported to Eionet-Water.

Both approaches assume that the mean concentrations of the national stations are normally distributed.

Approach 1

The number of stations needed to estimate the national mean within defined levels of confidence and precision can be calculated from the following equation.

M  =  (u/d)2(Vb + Vw/N)

This ensures that (on average) the confidence interval for the grand mean of site means will be ±d.

Where:

Vw	Best estimate of within-site variance

Vb	Best estimate of between-site variance

u	Standard Normal deviate for required two-sided confidence level - for example,  u = 1.96 for 95% confidence, = 1.645 for 90% confidence, = 0.674 for 50 % confidence.

d	Precision in the estimation of the national site mean.

N	Number of samples taken per site

M	Number of Eionet-Water sites

Approach 2

Alternatively the actual confidence interval for the grand mean of the national site means can be calculated from the number of stations reported to Eionet-Water. Rearranging the above equation we get:

d = u({[(Vb + Vw/N)]/M}

The results of applying approach 2 to the orthophosphate data in 2003 are summarised in Table 1 and depicted in Figures 1 and 2.

Figure 1

Figure 2

Table 1

|  | Mean number of samples per site | Number of sites | Lower 90% Confidence interval | Grand mean of site means | Upper 90% Confidence interval | Confidence interval as % of mean |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | mg P/l | mg P/l | mg P/l |  |
| AT | 11.4 | 226 | 0.023 | 0.028 | 0.033 | 18.1 |
| BE | 17.5 | 20 | 0.341 | 0.548 | 0.755 | 37.8 |
| BG | 10.3 | 108 | 0.140 | 0.165 | 0.191 | 15.5 |
| CS | 10.9 | 38 | 0.067 | 0.087 | 0.108 | 23.2 |
| CZ | 11.6 | 72 | 0.124 | 0.150 | 0.176 | 17.2 |
| DE | 22.3 | 147 | 0.064 | 0.072 | 0.079 | 10.4 |
| DK | 28.8 | 43 | 0.045 | 0.060 | 0.074 | 24.3 |
| EE | 9.6 | 53 | 0.033 | 0.057 | 0.080 | 41.0 |
| ES | 5.0 | 169 | 0.090 | 0.135 | 0.179 | 32.9 |
| FI | 8.8 | 158 | 0.015 | 0.018 | 0.020 | 16.8 |
| FR | 9.9 | 355 | 0.080 | 0.097 | 0.113 | 16.9 |
| GB | 13.3 | 206 | 0.280 | 0.337 | 0.395 | 17.0 |
| HR | 14.1 | 25 | 0.032 | 0.048 | 0.063 | 33.2 |
| HU | 31.1 | 95 | 0.226 | 0.300 | 0.374 | 24.8 |
| IT | 9.7 | 156 | 0.069 | 0.087 | 0.106 | 20.9 |
| LT | 12.0 | 65 | 0.094 | 0.164 | 0.234 | 42.7 |
| LV | 10.6 | 58 | 0.035 | 0.044 | 0.052 | 19.9 |
| NO | 1.6 | 153 | 0.001 | 0.006 | 0.012 | 85.6 |
| PL | 15.1 | 136 | 0.106 | 0.128 | 0.151 | 17.3 |
| SE | 12.2 | 116 | 0.010 | 0.013 | 0.016 | 21.1 |
| SI | 8.0 | 24 | 0.018 | 0.076 | 0.134 | 76.5 |
| SK | 7.6 | 31 | 0.122 | 0.187 | 0.252 | 34.6 |

The figures show that the most imprecise estimates of the national station mean orthophosphate concentrations arise from Norway, Belgium and Slovenia. For Norway this may be because sampling frequency is low (for many sites 1 sample a year), standard deviations were not provided for those sites with more than 1 sample and there was relatively high variability between site means. It should, however, be pointed out that the mean station orthophosphate concentration for Norway was the lowest of the countries, and whilst the percentage (of the mean) confidence intervals was very high, the actual confidence intervals expressed as concentrations were also very small.

Part of the EEA assessment on nutrients in rivers entails the comparison of concentrations between countries. This is done by the face-value classification of concentrations at the stations level. If this were to be done on the basis of comparing national station means then the differences between the countries could be statistically tested for significance.

For example, the grand site means for Belgium and GB, and Denmark and Estonia are not significantly different, whereas those for Czech Republic and Hungary, and Serbia and Bulgaria are significantly different at the 95 % level of confidence.

2.	Estimation of the number of years data required to detect linear trends in determinand concentrations with different levels of confidence

The EEA also requires to know whether quality is becoming better or worse. This is done at different levels of aggregation of data: European, regional, national and station levels. This requires an analysis of trends in concentrations over time.

For this analysis the number of years required to detect significant linear trends in national orthophosphate concentrations has been estimated from the data submitted by countries for 2003.

The basic equation for this calculation has been taken from WRc’s Sampling handbook (Ellis 1989).

Y3f = 48 {u*s/T}2

Where f = sampling frequency per year

Y = number of years

T = magnitude of linear trend to be detected in mg/l per year

s = short-term standard deviation

u = Standard Normal deviate for required two-sided confidence level.

Re-arranging the equation gives:

Y = 3([(48 {u*s/T}2)/f]

Two values of “T” have been used: values equivalent to 2 % and 10 % of the national station mean concentration.

f is the average sampling frequency for a country in 2003.

s (or standard error in this case) was calculated from:

s  =  ([Vb/M + Vw/(M(N)]

Where:

Vw	Best estimate of within-site variance

Vb	Best estimate of between-site variance

N	Number of samples taken per site

M	Number of Eionet-Water sites

The results are summarised in Table 2 and depicted in Figure 3.

Table 2

|  | Mean number of samples per site | Number of sites | Grand site Mean | 2% of grand mean | 10% of grand mean | Number of years to detect a linear trend of 2% of mean concentration a year | Number of years to detect a linear trend of 10% of mean concentration a year |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | mg P/l | mg P/l | mg P/l | 90 % confidence | 90 % confidence |
| AT | 11.4 | 226 | 0.028 | 0.001 | 0.003 | 7 | 2 |
| BE | 17.5 | 20 | 0.548 | 0.011 | 0.055 | 10 | 3 |
| BG | 10.3 | 108 | 0.165 | 0.003 | 0.017 | 7 | 2 |
| CS | 10.9 | 38 | 0.087 | 0.002 | 0.009 | 8 | 2 |
| CZ | 11.6 | 72 | 0.150 | 0.003 | 0.015 | 7 | 2 |
| DE | 22.3 | 147 | 0.072 | 0.001 | 0.007 | 4 | 1 |
| DK | 28.8 | 43 | 0.060 | 0.001 | 0.006 | 6 | 2 |
| EE | 9.6 | 53 | 0.057 | 0.001 | 0.006 | 13 | 4 |
| ES | 5.0 | 169 | 0.135 | 0.003 | 0.013 | 14 | 5 |
| FI | 8.8 | 158 | 0.018 | 0.0004 | 0.002 | 7 | 3 |
| FR | 9.9 | 355 | 0.097 | 0.002 | 0.010 | 7 | 2 |
| GB | 13.3 | 206 | 0.337 | 0.007 | 0.034 | 6 | 2 |
| HR | 14.1 | 25 | 0.048 | 0.001 | 0.005 | 10 | 3 |
| HU | 31.1 | 95 | 0.300 | 0.006 | 0.030 | 6 | 2 |
| IT | 9.7 | 156 | 0.087 | 0.002 | 0.009 | 8 | 3 |
| LT | 12.0 | 65 | 0.164 | 0.003 | 0.016 | 12 | 4 |
| LV | 10.6 | 58 | 0.044 | 0.001 | 0.004 | 8 | 3 |
| NO | 1.6 | 153 | 0.006 | 0.0001 | 0.001 | 38 | 13 |
| PL | 15.1 | 136 | 0.128 | 0.003 | 0.013 | 6 | 2 |
| SE | 12.2 | 116 | 0.013 | 0.0003 | 0.001 | 8 | 3 |
| SI | 8.0 | 24 | 0.076 | 0.002 | 0.008 | 21 | 7 |
| SK | 7.6 | 31 | 0.187 | 0.004 | 0.019 | 12 | 4 |

As would be expected it would only be relatively big changes in grand mean concentrations that would be detectable within a few years, and slower changes would take longer to detect. For example in Denmark a 10 % linear change in mean orthophosphate concentration a year would be detectable in around 2 years with a 90% confidence whereas a 2 % change a year would be detectable in 6 years. For Norway, even large changes (10%) in mean concentrations (a 0.6 µg P/l a year change in the mean concentration of 6 µg P/l) would not be detectable for 13 years. In the Norwegian context this may well be acceptable as concentrations are very low, and there would have to be very large increases before concentration became a concern.

Figure 3

3.	How representative are data from Eionet stations of quality in individual catchments?

As stated above Eionet water was designed to obtain representative information on water quality in water bodies at the national level. The aim is now to make information for SOE-WISE to be also representative of catchments.

To aid the discussion on what is needed to make reported information representative of catchments, an assessment has been made on how current Eionet stations are of a particular catchment, and of the country as a whole. The data used were nitrate concentrations in 2000 measured at:

- Eionet-water monitoring sites in the river Thames catchment in England and Wales (Thames Eionet sites);

- Monitoring sites in the Thames catchment used by the EA of England and Wales to assess the general quality of rivers (Thames GQA sites);

- Eionet-Water stations in England and Wales as a whole;

- GQA stations in England and Wales as a whole.

The results are illustrated in Figure 4 and tabulated in Table 3.

Table 3 	Comparison of grand mean of site mean nitrate concentrations in 2000 with 90% confidence intervals for Eionet-Water and GQA river stations in the Thames catchment and in England and Wales

|  | Mean number of samples per site | Number of sites | Lower 90% Confidence interval | Grand mean of site means | Upper 90% Confidence interval |
| --- | --- | --- | --- | --- | --- |
| Eionet-Thames | 38 | 11 | 27.5 | 38.2 | 48.9 |
| GQA-Thames | 37 | 193 | 30.9 | 32.3 | 33.8 |
| Eionet-EW | 13 | 153 | 20.7 | 23.4 | 26.2 |
| GQA-EW | 37 | 8912 | 23.0 | 23.4 | 23.7 |

Figure 3

Figure 3 shows that the grand mean nitrate concentration for the Thames catchment based on 193 GQA stations is 15 % less than that derived from the 11 Eionet-Water stations. As would be expected from the greater number of stations, the 90% confidence intervals are also smaller around the GQA grand mean than that derived from Eionet-Water stations. However the difference in the mean concentrations are not significantly different (95% level of confidence). There might therefore be some risk of “misclassifying” and “misrepresenting” the Thames catchment if it were to be based on Eionet stations alone and on the use of face-value average concentrations without consideration of associated concentration confidence limits.

For England and Wales as a whole the 153 Eionet-Water stations give virtually the same grand mean nitrate concentration as that calculated from the 8912 stations in the GQA scheme. This perhaps illustrates that the selection of Eionet stations for England and Wales was reasonably representative of the country as a whole if one of the objectives of Eionet-water was to obtain national mean concentrations of nitrate. The difference in mean nitrate concentrations for the Eionet stations for the Thames catchment and for England and Wales are significantly different (95% level of confidence) as are those between the GQA stations in the Thames catchment and England and Wales as a whole. This illustrates that nitrate concentrations in the Thames river catchment are significantly higher than the average for England and Wales as a whole, and this would be demonstrated by the data arising from the present number of stations in Eionet-Water.

In summary:

- The current Eionet stations are not fully representative of the Thames catchment in terms of nitrate concentrations in rivers.

- The current Eionet stations would be representative of the average situation in England and Wales in terms of nitrate concentrations in rivers.

Version 2

7 November 2006