|  | EUROPEAN TOPIC CENTRE ON WATER |  |
| --- | --- | --- |

Guidance on Updating of Priority Data Flows for EUROWATERNET – Transitional, Coastal and Marine Waters and the Population of WATERBASE

Authors: Ruth Cullingford, WRC and Birger Bjerkeng, NIVA

EEA project manager: Anita Künitzer

Table of Contents

1. Introduction	3

2.	EUROWATERNET concept	3

3.	Water Types - Water Framework Directive definitions	4

4.	Types of Monitoring Station	5

5.	Number of stations	6

6.	Determinands and supporting information required for EUROWATERNET	7

7.	Riverine loads and direct discharges into marine waters	16

8.	Delivery of Data Files	24

9.	Timetable	24

10.	References	25

# 1. Introduction

Significant progress has been made in implementing EUROWATERNET as the process for priority data flow for the collection of European River, Lake and Groundwater data (Nixon et al., 1999). This process includes the development of the concept on data needed for water assessments, the development of reporting guidelines as well as country visits to reach common understanding of the process.  EUROWATERNET guidelines for Quantity and Emissions and related data flows are under development.  The EEA also requires timely, targeted, relevant and reliable information on Transitional, Coastal and Marine Waters for its assessments.

The EEA has already been working closely with the Marine Conventions to initiate data flows and a working database MARINEBASE (Nygaard et al., 2001) has been developed to store data provided by the Conventions. The table structures and data held in MARINEBASE will be updated and changed in 2003 for use in the EEA indicator reports and for the first data flow on transitional, coastal and marine data through the EUROWATERNET process. This database will be renamed WATERBASE-Transitional, Coastal and Marine Waters.

The EUROWATERNET-Transitional, Coastal and Marine Water guidelines detail the content and format of data required from both the Marine Conventions and each country.  The station classification system is applied to ensure that data from the same station type is comparable.

It is recognised that whilst countries already supply data to the Marine Conventions, the time series are somewhat incomplete. It is not the intention that the EUROWATERNET data flow should require countries to make duplicate supplies of data and so any data already submitted to the Marine Conventions need not be re-supplied through the EUROWATERNET process. It will be requested directly from the Marine Conventions. However, since Marine Convention data sets are incomplete and there is no ongoing process within Conventions to complete it, it is necessary to ask each country to supply any missing or additional data. The content and format of the data request is the same for both the Marine Conventions and each country.

# 2.	EUROWATERNET concept

EUROWATERNET is designed to give a representative assessment of water types and human pressures affecting the quality and quantity of water within each Member Country and across the EEA area.

EUROWATERNET is firmly based on existing national and international water monitoring networks. However, there are often large differences in national water monitoring networks because:

- they are established to meet national needs and priorities

- many are only ‘impact’ networks in relation to major point source discharges

- many only monitor nationally large or important water bodies

There are, therefore, very large differences in existing networks in terms of:

- objectives

- water body types monitored

- numbers of monitoring stations

- determinands measured

This is why the implementation of EUROWATERNET has been and will remain a step-by-step process, evolving and extending as national networks develop and change across Europe.

The existing MARINEBASE database represents a “first step in collecting and combining data from various sources into a common framework for presentation of environmental conditions” (Nygaard et al., 2001).  It closely reflects the data structures and fields used by the Marine Conventions and ICES. Data has been reported in various formats and data descriptions. The contents of MARINEBASE were updated in 2001 by data request and exchange with the Marine Conventions and NRCs. There is now a need to revise the structure of MARINEBASE and impose definite requirements on the content and format of data to be included in the database. Such definite requirements will be given by this guidance document.

The revised MARINEBASE will be renamed WATERBASE-Transitional, Coastal and Marine Waters (TCM) and its content will focus on data to be used in the production of indicator-based reports and other environmental assessments at both the regional and European scale, requested through the EUROWATERNET data flow procedure.  It will also reflect the general format and appearance of the other water datasets.  WATERBASE-TCM will have four main elements:

- details of the monitoring stations’ physical characteristics

- disaggregated water column, biota and sediment chemical quality data

- details of proxy pressures applicable to each monitoring station, and

- data on riverine and direct input loads

Much of the data stored in the existing version of MARINEBASE is supplemental to the needs of EUROWATERNET and is not specifically required.  It is anticipated that the number of look-up tables in the database will be reduced.

The EEA intends to continue collaborations with the Marine Conventions in gathering data under EUROWATERNET, in order to prevent countries from making duplicate submissions of data.

The EUROWATERNET data request will be an annual event and the data will ultimately be uploaded annually from the working database (WATERBASE-TCM) to the Reference WATERBASE, along with the other water datasets. In the near future we will also be requesting data on the biological communities of transitional, coastal and marine waters. These aspects will also be simultaneously developed for rivers and lakes.

# 3.	Water Types - Water Framework Directive definitions

At the very basic level we need to distinguish between transitional, coastal and marine waters. The Water Framework Directive (WFD) definitions for transitional and coastal waters are being used:

“Transitional waters are bodies of surface water in the vicinity of river mouths which are partly saline in character as a result of their proximity to coastal waters but which are substantially influenced by freshwater flows.”

“’Coastal water’ means surface water on the landward side of a line, every point of which is at a distance of one nautical mile on the seaward side from the nearest point of the baseline from which the breadth of territorial waters is measured, extending where appropriate up to the outer limit of transitional waters.”

Marine waters would then by default be “waters seaward of coastal waters”.

The WFD CIS Working Group 2.4 (COAST) provides further details in “Guidance on Typology, Reference Conditions and Classification Systems for Transitional and Coastal Waters”.

One key distinguishing physical characteristic of transitional waters (based on the WFD definition) is salinity.  The width of coastal waters varies as the baseline from which the breadth of territorial waters is measured differs from country to country.  Some include offshore islands as the baseline, which can mean that the coastal water can extend tens of kilometres offshore, and certainly more than the 1 nautical mile limit in the definition.  For each monitoring station we require both the distance from the nearest mainland and distance from nearest land (if it is close to an offshore island).

# 4.	Types of Monitoring Station

The definition of the type of monitoring stations to be included in EUROWATERNET Transitional, Coastal and Marine Waters are as follows:

Reference stations would occur in waters that are minimally impacted by human activity.

Reference stations in transitional waters would have catchments or drainage basins with little or no human activity and the percentage of natural landscape would be higher than 90%.  They would also be expected to be minimally impacted through inflow of water, which is impacted by human activity, from the adjacent coastal or marine waters.

Reference stations in coastal waters would also be associated with River Basin Districts with little or no human activity and the percentage of natural landscape would be higher than 90%.  In addition, it would be expected that the adjacent marine waters with which water is exchanged would be minimally impacted by human activity.

In terms of physico-chemical determinands and hazardous substances (including WFD Priority Substances, Dangerous Substances Directive Lists I and II, and the Marine Conventions’ lists of priority substances) that occur naturally, it might be expected that the concentrations measured at these stations would give an indication of ‘background levels’.

Transitional, coastal and marine waters remote from the main centres of human activity may of course still be impacted by the atmospheric deposition of contaminants, in particular volatile synthetic substances.  In these waters this may be the principal or only pollution source and data from such areas might be used to assess the significance of atmospheric deposition.  However, stations in such waters would not qualify as reference stations if the deposited contaminants resulted in a measurable ecological effect.

Representative stations would reflect the general quality of the transitional and coastal water body and marine water area with respect to pressures placed upon them.  Stations selected under EUROWATERNET should be representative of the physico-chemical quality elements, such as nutrients and organic pollution indicators, and also representative of hazardous substances, including those detailed on the WFD Priority Substance List, Lists I and II of the Dangerous Substances Directive and the Marine Conventions’ lists of priority substances (see Annex 1).  The water quality at these stations would be influenced by diffuse and/or point sources of pollution depending on human activities upstream and in adjacent waters.  It would be expected that pollutants from point sources would be fully mixed and diluted within the ambient water flow/volume.  These stations may be included within National Networks used to obtain an overview of the numbers and concentrations of hazardous substances present and of the general levels of nutrients and organic pollution indicators.  This type of station is likely to be included in ‘surveillance’ monitoring programmes as required by the WFD.  Many of these stations may therefore have a long time series of data.

Under EUROWATERNET Impact an additional type of monitoring station is identified.

Impact stations are monitoring stations within the zone (area or volume of water) where initial mixing of emissions from a particular discharge or concentrated group of discharges takes place with the receiving waters (sometimes also called ‘hot spots’).  Concentrations of determinands would be expected to be relatively high (‘worst-case’ concentrations) at these stations. These stations may be used by the regulatory authorities to assess the compliance of discharges within standards or limits.  Thus,  monitoring at these stations may in some cases be limited to those substances present within any particular discharge.  Stations of this type are likely to be included in ‘operational’ monitoring programmes as required by the WFD.  Many of these stations may therefore have a relatively long time series of data and as such should be included in the EUROWATERNET reporting procedure.  Data is not requested from monitoring stations established for ad-hoc purposes, such as for investigative monitoring, and which are sampled for only a limited time period.

Countries should report data from all of the above station types.  Comparisons will be made by station type in order that like is compared with like.

# 5.	Number of stations

Our aim is not only to make EUROWATERNET representative of the pressures on transitional, coastal and marine waters but also of the numbers and types of water bodies and areas.  This is consistent with the aim of surveillance monitoring under the WFD, which requires the monitoring of “sufficient water bodies to provide an assessment of the overall surface water status within each catchment or sub-catchments within the River Basin District.”

EU Member States have started the process of typifying their transitional and coastal waters to establish the number of water body types and which will require assessment and/or monitoring under the WFD.  As every national River Basin District will require a plan, it is likely that the assessment and/or monitoring of quality in some countries will become more geographically spread at the national level than it is at present.

The EEA is currently reliant on information submitted by the Marine Convention Contracting Parties to ICES and/or Commissions, supplemented by additional national data.  It is likely therefore that there is more information available at the national level than is submitted to the Marine Conventions and ICES.

EUROWATERNET will require monitoring data for the specified determinands from all representative, reference and impact stations in national transitional and coastal water monitoring programmes except data from investigative monitoring.  Ultimately, an assessment will have to be undertaken to determine how representative this information is of the transitional and coastal water bodies at the national level.  For example, it will be of use to know how many transitional waters are monitored compared to the total number of transitional waters in a country or the length of coastal waters monitored as a proportion of the total national coastline.

# 6.	Determinands and supporting information required for EUROWATERNET

It is our aim to make proposals for determinands and supporting information consistent as far as possible with other requirements and initiatives such as the WFD and EUNIS.  We will be requesting data from three different environmental compartments: water column, sediment and biota.  It will be necessary to know what compartments are sampled at each station.  Not all stations will sample all compartments.

The following Tables list the information we are requesting under EUROWATERNET- Transitional, Coastal and Marine Waters.

Table 6.1 denotes the physical characteristic data required for each transitional, coastal and marine water monitoring station.

Tables 6.2, 6.3 and 6.4 contain details of the data relating to concentrations of determinands in water column, biota and sediment measured at each station.  The concentration values of each determinand are requested.

Table 6.5 contains a list of the proxy pressure information required.

Data should be submitted using Excel spreadsheets or ASCII text files (tab or semi-colon separated) based on the structure and layout of the Excel templates provided.  (EWN_TCM_Data.xls.)

Table 6.1	Physical characteristics of EUROWATERNET Transitional, 			Coastal and Marine Water stations (to be submitted only once			but updated if appropriate)

| Field Name | Description | Type / Format |
| --- | --- | --- |
| WATER_TYPE | Water Body Type As defined by the WFD: T = Transitional water C = Coastal water M = Marine water. | Text 1 char |
| TYPE_DESC | Water Body Type Description Additional water body description, e.g. Estuary, Coastal Lagoon, Embayment. | Text 50 chars |
| STN_ID | National Station ID Station/sampling area indicator unique at national level. This should be the same ID as previously supplied. A station may be a geographically fixed location. A station may also be a broader area in which actual sampling locations may vary from survey-to-survey. A station may also be an area with a defined salinity range within which samples have to be taken. Areas will however be recorded and reported as a discrete sampling location. | Text 50 chars |
| STN_ NAME | National Station Name | Text 50 chars |
| STN_REPORTING | Station Reporting Purpose The monitoring station is used for the following reporting purposes: N = National purposes MC = Marine Conventions EC = European Commission Multiple entries separated by commas allowed (e.g. N,EC). | Text 10 chars |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| WATER_NAME | Water Body Name | Text 50 chars |
| SEA_NAME | Marine Water Body Name Consistent with Marine Convention nomenclature. | Text 50 chars |
| CATCH_NAME | Catchment Name Major river catchment/basin draining into transitional or coastal water. | Text 50 chars |
| COAST_MAIN | Mainland Coast Distance from nearest mainland coast expressed in kilometres (km). | Number 2 decimal places |
| COAST_CLOSE | Closest Coast Distance from closest coast expressed in kilometres (km). (If different from COAST_MAIN) | Number 2 decimal places |
| REGION | Region Region name where the transitional or coastal water is located. | Text 50 chars |
| LONG | Longitude (X) International geographical co-ordinates of the monitoring station/area in decimal degrees format. | Number 5 decimal places |
| LAT | Latitude (Y) International geographical co-ordinates of the monitoring station/area in decimal degrees format. | Number 5 decimal places |
| STN_TYPE | EUROWATERNET Station Type B = Reference station R(PHYS) = Station representative of general conditions in terms of physico-chemical quality elements (e.g nutrients, organic matter) I(PHYS) = Station impacted directly by discharges affecting physico-chemical conditions R(HZ) = Station representative of general conditions in terms of hazardous substances I(HZ) = Station impacted directly by specific discharges containing hazardous substances Station can be of more than one type – separate entries with commas, e.g. B,R(PHYS). | Text 30 chars |
| MatRIX | Matrix Environmental compartments measured at station. Any combination of codes: W = Water Column B = Biota S = Sediment Separate entries with commas (e.g. W,B,S). | Text 10 chars |
| Salinity_mean | Mean Annual Salinity Expressed in practical salinity units (psu). | Number 4 decimal places |
| Salinity_min | Minimum Annual Salinity Expressed in practical salinity units (psu). | Number 4 decimal places |
| Salinity_max | Maximum Annual Salinity Expressed in practical salinity units (psu). | Number 4 decimal places |
| TEMPERATURE | Mean Annual Temperature Expressed in degrees Celsius (oC). | Number 2 decimal places |
| TIDAL_MEAN | Mean Tidal Range At the transitional or coastal station expressed in metres (m). | Number 2 decimal places |
| DEPTH | Mean Annual Depth Expressed in metres (m). | Number 2 decimal places |
| RESIDENCE | Residence Time Of transitional or coastal water body, expressed in number of days. | Integer |
| MIXING | Mixing Characteristics At transitional water monitoring station: FM = Fully Mixed PM = Partially Mixed VS = Vertically Stratified | Text 2 chars |
| REMARKS | Remarks Additional comments. | Text 100 chars |

Table 6.2	Concentrations of physico-chemical and hazardous substances 		in water (to be submitted annually)

| Field Name | Description | Type / Format |
| --- | --- | --- |
| STN_ID | National Station ID Station indicator unique at national level. This should be the same ID as supplied in Table 6.1. | Text 50 chars |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| YEAR | Year Calendar year when sample was taken (YYYY). | Integer |
| MONTH | Month Month when sample was taken (1-12). | Integer |
| DAY | Day Day of month when sample was taken (1-31). | Integer |
| DEPTH | Sampling depth Expressed in metres (m). | Number 1 decimal |
| THERM_POS | Vertical Position Relative to Thermocline AT = Above Thermocline IT = In Thermocline BT = Below Thermocline | Text 2 chars |
| HALO_POS | Vertical Position Relative to Halocline AH = Above Halocline IH = In Halocline BH = Below Halocline | Text 2 chars |
| SAMPLE_ID | Sample Identifier Unique number required if multiple samples taken within station-country-date-determinand. | Text 8 chars |
| CAS_No | Chemical Abstract Service Number Of hazardous substance listed in Annex 1. | Text 20 chars |
| DETERMINAND | Determinand Name of element or chemical component analysed in format as detailed in Annexes 1 and 2. | Text 50 chars |
| UNIT | Unit of Measurement Hazardous substances listed in Annex 1 expressed in microgrammes per litre (µg/l). Physico-chemical substances expressed in format as detailed in Annex 2. | Text 20 chars |
| CONC | Concentration Of determinand in sample. | Number 4 decimal places |
| SALINITY | Salinity Of sample or salinity to which sample concentration is normalised, expressed in practical salinity units (psu). | Number 1 decimal place |
| <LoD | Less than Limit of Detection Flag Flag to indicate sample below analytical limit of detection in format -999. | Integer |
| LoD | Limit of detection That concentration for which there is a desirably small probability that the determinand will not be detected (usually detected with 95% confidence). Expressed in same units as CONC. | Number 4 decimal places |
| DTR_LMT | Limit of determination The smallest concentration that can be distinguished from the analytical blank at a chosen level of statistical confidence (usually 95%). Expressed in same units as CONC. | Number 4 decimal places |
| REMARKS | Remarks Any additional comments. | Text 100 chars |

Table 6.3	Concentrations of hazardous substances in biota (to be submitted annually)

| Field Name | Description | Type / Format |
| --- | --- | --- |
| STN_ID | National Station ID Station indicator unique at national level. This should be the same ID as supplied in Table 6.1. | Text 50 chars |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| YEAR | Year Calendar year when sample was taken (YYYY). | Integer |
| MONTH | Month Month when sample was taken (1-12). | Integer |
| DAY | Day Day of month when sample was taken (1-31). | Integer |
| SPECIES | Species Code See Annex 4. | Text 8 chars |
| TISSUE | Tissue Code See Annex 5. | Text 2 chars |
| SAMPLE_ID | Sample Identifier Unique number required if multiple samples taken within station-country-date-determinand. | Text 8 chars |
| CAS_No | Chemical Abstract Service Number Of hazardous substances listed in Annex 1. | Text 20 chars |
| DETERMINAND | Determinand Name of element or chemical component analysed from the list in Annex 1. | Text 50 chars |
| UNIT | Unit of Measurement Expressed as weight ratio microgrammes per kilogramme dry weight (µg/kg dw) or microgrammes per kilogramme fresh weight (µg/kg fw). | Text 20 chars |
| BASIS | Basis of Measurement D = Dry W = Wet L = Lipid (fat). | Text 1 char |
| CONC | Concentration Of determinand in sample. | Number 4 decimal places |
| <LoD | Less than Limit of Detection Flag Flag to indicate sample below analytical limit of detection in format -999. | Integer |
| LoD | Limit of detection That concentration for which there is a desirably small probability that the determinand will not be detected (usually detected with 95% confidence). Expressed in same units as CONC. | Number 4 decimal places |
| DTR_LMT | Limit of determination The smallest concentration that can be distinguished from the analytical blank at a chosen level of statistical confidence (usually 95%). Expressed in same units as CONC. | Number 4 decimal places |
| DRY_FRESH_RATIO | Ratio of Dry Weight to Fresh Weight Expressed as percentage (%). | Number 2 decimal places |
| FAT_PRC | Fat Content Expressed as percentage (%) of total dry matter. | Number 2 decimal places |
| REMARKS | Remarks Any additional comments. | Text 100 chars |

Table 6.4	Concentrations of hazardous substances in sediment (to be submitted annually)

| Name | Description | Type / Format |
| --- | --- | --- |
| STN_ID | National Station ID Station indicator unique at national level. This should be the same ID as supplied in Table 6.1. | Text 50 chars |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| YEAR | Year Calendar year when sample was taken (YYYY). | Integer |
| MONTH | Month Month when sample was taken (1-12). | Integer |
| DAY | Day Day of month when sample was taken (1-31). | Integer |
| SAMPLE_ID | Sample Identifier Unique number required if multiple samples taken within station-country-date-determinand. | Text 8 chars |
| CAS_No | Chemical Abstract Service Number Of hazardous substances listed in Annex 1. | Text 20 chars |
| DETERMINAND | Determinand Name of element or chemical component analysed from the list in Annex 1. | Text 50 chars |
| UNIT | Unit of Measurement Expressed as weight ratio microgrammes per kilogramme dry weight (µg/kg dw) or microgrammes per kilogramme fresh weight (µg/kg fw). | Text 20 chars |
| CONC | Concentration Of determinand in sample. | Number 4 decimal places |
| <LoD | Less than Limit of Detection Flag Flag to indicate sample below analytical limit of detection in format -999. | Integer |
| LoD | Limit of detection That concentration for which there is a desirably small probability that the determinand will not be detected (usually detected with 95% confidence). Expressed in same units as CONC. | Number 4 decimal places |
| DTR_LMT | Limit of determination The smallest concentration that can be distinguished from the analytical blank at a chosen level of statistical confidence (usually 95%). Expressed in same units as CONC. | Number 4 decimal places |
| BOTTOM_DEPTH | Bottom Depth At sampled site expressed in metres (m). | Number 2 decimal places |
| SAMPLER | Sampling Equipment Used | Text 50 chars |
| SED_DEPTH_TOP | Top of Analysed Sediment Layer Measured from the sediment surface, expressed in centimetres (cm). Value will be zero if same as sediment surface. | Integer |
| SED_DEPTH_BOTTOM | Bottom of Analysed Sediment Layer Measured from top of analysed sediment layer, expressed in centimetres (cm). | Integer |
| ORG_C | Organic Carbon Expressed as percentage (%) of total dry weight. | Number 2 decimal places |
| GRAIN_TYPE | Sediment Type Sediment type description if no analysis of grain size. M = Mud FS = Fine Sand MS = Middle Sand CS = Coarse Sand G = Gravel | Text 2 chars |
| FRACTION | Size Fraction Analysed Upper limit of particle size in analysed fraction, expressed in micrometres (µm). Blank if whole sediment has been analysed. | Integer |
| DRY_WET_RATIO | Ratio of Dry Weight to Wet Weight Expressed as percentage (%). | Number |
| BASIS | Dry/Wet Weight Result Flag D = Dry Weight W = Wet Weight | Text 1 char |
| REMARKS | Remarks Any additional comments. | Text 100 chars |

Table 6.5	Proxy pressure information required for each monitoring station  		(to be submitted once and updated if appropriate)

| Name | Description | Type / Format |
| --- | --- | --- |
| STN_ID | National Station ID Station indicator unique at national level. This should be the same ID as supplied in Table 6.1. | Text 50 chars |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| POPULATION | Population Density In the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as capita per square kilometre (capita/km2). | Number 2 decimal places |
| Land use information based on Corine Land Cover or equivalent |
| URBAN | Urban Area Urbanisation in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| WETLAND | Wetland Wetland in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| NATURE | Natural Land Natural land in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| FOREST | Forest Forest in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| AGRI_TOT | Total Agricultural Land Total Agricultural area in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| AGRI_OTHER | Other Agricultural Land Other Agricultural area in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| ARABLE | Arable Land Arable land in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| PASTURE | Pastural Land Pastural land area in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| OTHER | Other Land Use Other land use in the catchment / drainage basin upstream of the transitional water or within the River Basin District to which the coastal water has been assigned. Expressed as percentage (%). | Number 2 decimal places |
| Other anthropogenic activities (if any) |
| SEWAGE_DISCHARGE | Sewage Discharge Direct discharges* from sewage treatment works to the water body. U = UWWT NU = Non-UWWT BU = Both | Text 10 chars |
| INDUST_DISCHARGE | Industrial Discharge Direct discharges* from industry to the water body. E = EPER NE = Non-EPER BE = Both | Text 10 chars |
| OTHER_DISCHARGE | Other Discharge Direct discharges* from other sources to the water body. Y = Yes N = No | Text 1 char |
| OIL_EXTRACT | Oil Extraction Exploration for or extraction of oil. Y = Yes N = No | Text 1 char |
| GAS_EXTRACT | Gas Extraction Exploration for or extraction of gas. Y = Yes N = No | Text 1 char |
| SPOIL | Dredged Spoil Disposal Ground Y = Yes N = No | Text 1 char |
| WASTE | Waste Disposal Ground Y = Yes N = No | Text 1 char |
| LANDFILL | Landfill Water body directly impacted by leachate from landfill disposal sites. Y = Yes N = No | Text 1 char |
| MARICULTURE | Mariculture Fish and shellfish farming. Y = Yes N = No | Text 1 char |
| FISHING | Fishing Commercial fishing activity. Y = Yes N = No | Text 1 char |
| MARINA | Marina Presence of a marina. Y = Yes N = No | Text 1 char |
| PORT | Port Presence of port facilities. Y = Yes N = No | Text 1 char |
| OTHER | Any Other Activities Y = Yes N = No | Text 1 char |
| REMARKS | Remarks Any additional comments. | Text 100 chars |

*  The OSPAR RID Guidelines define direct discharge as:

“a mass of a determinand discharged to the maritime area from land-based sources (sewage effluents, industrial effluents or other) per unit of time at a point on a coast or to an estuary downstream of the point at which the riverine estimate of input is made.”

# 7.	Riverine loads and direct discharges into marine waters

We also require aggregated information on the riverine loads and the loads from direct discharges to Europe’s Seas.  This is to be based on the information submitted to the Regional Sea Conventions and is summarised below in Table 7.1.  Some of this information is reported on an annual basis (such as for the OSPAR RID programme) whilst information for the Baltic Pollution Load Compilation is only collected on a 5-yearly basis.  Our aim is to gain as complete a temporal (years) and spatial (countries and sea regions) coverage as possible.

We are asking for annually aggregated load information for each river station used in calculating riverine loads entering your sea (see Table 7.2). We require the national station identifiers and details of the sea area into which the river discharges, along with details of the regional sea that it is part of (e.g. Celtic Sea, Bothnian Bay).  We are also asking for the average discharge/flow at each river station for each year (either measured or calculated), and the long term annual averages for each station (see Table 7.3).  The flow information is required in order to interpret the riverine load data.  For direct discharges we are requesting annually aggregated load data for each sea area.  Thus the identifier used for the sea area in terms of direct discharges must equate to the identifier used for sea area into which the riverine load discharges.  This is to ensure that we can relate riverine loads to direct discharge loads.

As for the EUROWATERNET data, this information will be used to formulate indicators for use in the EEA’s assessments and reports.

It should be noted that the EEA/ETC-WTR has developed EUROWATERNET-Emissions, which will be used in the future to collect disaggregated source-oriented information on pollutant loads to surface waters.  This will eventually be used to supplement the load information requested here.  EUROWATERNET-Emissions is also consistent with the requirements of the IPPC Directive (e.g. for an EPER) and with the HARP initiative.

We ask that each country supplies data using the templates provided (EWN_TCM_Inputs.xls).  Each template refers to one Marine Convention and details the relevant countries and sea areas for which data is required.

Table 7.1	Determinands required for riverine and direct load assessments for Marine Conventions

| Determinand | Units | OSPAR RID | HELCOM PLC | MAP | Black Sea |
| --- | --- | --- | --- | --- | --- |
| Nitrate | Tonnes/yr | (M | (M1, V4 |  | ( |
| Nitrite | Tonnes/yr |  | (V |  | ( |
| Orthophosphate | Tonnes/yr | (M | (M1, V4 |  | ( |
| Total nitrogen | Tonnes/yr | (M | (M6 | (1, 2, 7, 8 | ( |
| Total phosphorus | Tonnes/yr | (M | (M6 | (1, 2, 7, 8 | ( |
| Ammonia | Tonnes/yr | (M | (M1, V4 |  | ( |
| Total mercury | kg/yr | (M | (M | (1, 2, 7 |  |
| Total cadmium | kg/yr | (M | (M |  | ( |
| Total zinc | kg/yr | (M | (M | (1, 2, 7 |  |
| Total lead | kg/yr | (M | (M | (1, 2, 7 | ( |
| Copper | kg/yr |  | (M |  | ( |
| Nickel | kg/yr |  | (M2, V5 |  |  |
| Chromium | kg/yr |  | (M2, V5 | (1, 2, 7 |  |
| Gamma-HCH | kg/yr | (M |  |  |  |
| Suspended particulate matter | Tonnes/yr | (M | ( V1, M3 | (1, 2, 7, 8 | ( |
| Salinity (in saline waters) | psu | (M |  |  |  |
| Flow | m3/sec | ( |  |  |  |
| Volume |  |  |  | (1, 2, 7, 8 |  |
| Hydrocarbons | Tonnes/yr | (R (PAHs and mineral oil strongly recommended) |  | (1, 2, 7 | ( |
| PCBs (the following congeners: IUPAC Nos 28, 52, 101, 118, 153, 138, 180); | kg/yr | (R |  |  |  |
| Other hazardous substances (particularly organohalogen compounds) | kg/yr | (R |  | (1, 8 |  |
| BOD-7 | Tonnes/yr |  | (M |  |  |
| BOD-5 |  |  |  | (1, 2, 7, 8 | ( |
| COD-Mn | Tonnes/yr |  | (V1 |  |  |
| COD-Cr | Tonnes/yr |  | (M2 | (1, 2, 7, 8 |  |
| TOC | Tonnes/yr |  | (V | (8 |  |
| AOX | Tonnes/yr |  | (V1, M2 |  |  |
| Radioactivity |  |  |  | (1, 2 |  |

RID	OSPAR’s Comprehensive Study on Riverine Inputs and Direct Discharges

PLC3	HELCOMS Pollution Load Compilation 1995

MAP	Survey of pollutants from land-based sources in the Mediterranean

M	Mandatory

R 	Recommended

V	Voluntary

1	Riverine inputs

2	Industrial effluents

3	Untreated municipal or industrial effluents

4	Municipal and industrial effluents

5	Riverine inputs and municipal effluents

6	Includes diffuse inputs from the coastal zone

7	Domestic sewage

8	Agricultural run-off

Table 7.2	Yearly riverine input loads

| Field Name | Description | Type / Format |
| --- | --- | --- |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| YEAR | Year Of aggregation period. | Integer |
| STN_ID | National Station ID Station/sampling area indicator unique at national level. | Text 50 chars |
| LONG | Longitude (X) International geographical co-ordinates of the monitoring station in decimal degrees format. | Number 5 decimal places |
| LAT | Latitude (Y) International geographical co-ordinates of the monitoring station in decimal degrees format. | Number 5 decimal places |
| STN_ NAME | National Station Name | Text 50 chars |
| RIVER_NAME | River Name In which loads are measured. | Text 50 chars |
| CATCH_NAME | Catchment Name Major river catchment or river basin name. | Text 50 chars |
| SEA_AREA_NAME_ID | Sea Area Name or ID Into which river discharges. | Text 50 chars |
| SEA_REGION_NAME | Regional Sea Name Of which Sea Area is a part of. | Text 50 chars |
| SEA_CONVENTION_AREA | Marine Convention Sea Area Name | Text 50 chars |
| Estimate | Estimate Lower estimate based on treating determinand values that are less than the limits of detection as zero. Upper estimate based on treating determinand values that are less than the limits of detection as values equivalent to the limit of detection value. | Number 4 decimal places |
| Nitrate | Nitrate Load of Nitrate expressed in kilotonnes (kt). | Number 4 decimal places |
| Nitrite | Nitrite Load of Nitrite: expressed in kilotonnes (kt). | Number 4 decimal places |
| Orthophosphate | Orthophosphate Load of Orthophosphate: expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Nitrogen | Total Nitrogen Load of Total Nitrogen expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Phosphorus | Total Phosphorus Load of Total Phosphorus expressed in kilotonnes (kt). | Number 4 decimal places |
| Ammonia | Ammonia Load of Ammonia expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Mercury | Total Mercury Load of Total Mercury expressed in tonnes (t). | Number 4 decimal places |
| Total Cadmium | Total Cadmium Load of Total Cadmium expressed in tonnes (t). | Number 4 decimal places |
| Total Zinc | Total Zinc Load of Total Zinc expressed in tonnes (t). | Number 4 decimal places |
| Total Lead | Total Lead Load of Total Lead expressed in tonnes (t). | Number 4 decimal places |
| Copper | Copper Load of Copper expressed in tonnes (t). | Number 4 decimal places |
| Nickel | Nickel Load of Nickel expressed in tonnes (t). | Number 4 decimal places |
| Chromium | Chromium Load of Chromium expressed in tonnes (t). | Number 4 decimal places |
| Gamma-HCH | Gamma-HCH Load of Gamma-HCH expressed in tonnes (t). | Number 4 decimal places |
| Suspended Particulate Matter | Suspended Particulate Matter Load of Suspended Particulate Matter expressed in tonnes (t). | Number 4 decimal places |
| Hydrocarbons | Hydrocarbons Load of Hydrocarbons expressed in kilotonnes (kt). | Number 4 decimal places |
| Detergents | Detergents Load of Detergents expressed in kilotonnes (kt). | Number 4 decimal places |
| Phenols | Phenols Load of Phenols expressed in kilotonnes (kt). | Number 4 decimal places |
| PCB-28 | PCB-28 Load of PCB-28 expressed in tonnes (t). | Number 4 decimal places |
| PCB-52 | PCB-52 Load of PCB-52 expressed in tonnes (t). | Number 4 decimal places |
| PCB-101 | PCB-101 Load of PCB-101 expressed in tonnes (t). | Number 4 decimal places |
| PCB-118 | PCB-118 Load of PCB-118 expressed in tonnes (t). | Number 4 decimal places |
| PCB-153 | PCB-153 Load of PCB-153 expressed in tonnes (t). | Number 4 decimal places |
| PCB-138 | PCB-138 Load of PCB-138 expressed in tonnes (t). | Number 4 decimal places |
| PCB-180 | PCB-180 Load of PCB-180 expressed in tonnes (t). | Number 4 decimal places |
| Total PCBs | Total PCBs Load of Total PCBs expressed in tonnes (t). | Number 4 decimal places |
| Other Hazardous Substances | Other Hazardous Substances Load of Other Hazardous Substances expressed in tonnes (t). Provide name and CAS No of any additional hazardous substances monitored. | Number 4 decimal places |
| BOD-7 | BOD-7 Load of BOD-7 expressed in kilotonnes (kt). | Number 4 decimal places |
| BOD-5 | BOD-5 Load of BOD-5 expressed in kilotonnes (kt). | Number 4 decimal places |
| COD-Mn | COD-Mn Load of COD-Mn expressed in kilotonnes (kt). | Number 4 decimal places |
| COD-Cr | COD-Cr Load of COD-Cr expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Organic Carbon | Total Organic Carbon Load of Total Organic Carbon expressed in kilotonnes (kt). | Number 4 decimal places |
| Organic Compounds | Organic Compounds Load of Organic Compounds expressed in kilotonnes (kt). | Number 4 decimal places |
| Tritium | Tritium Load of Tritium expressed in Becquerels (Bq). | Number 4 decimal places |
| Radionuclides | Radionuclides Load of Radionuclides expressed in Becquerels (Bq). Provide name of any additional radionuclides monitored. | Number 4 decimal places |
| Average Riverine flow for the Year | Average Riverine flow for the Year Expressed in cubic metres per second (m3/sec). | Number 2 decimal places |
| Long Term Annual Average Riverine Flow | Long Term Annual Average Riverine Flow Expressed in cubic metres per second (m3/sec). | Number 2 decimal places |
| Remarks | Remarks Additional comments. | Text 100 chars |

Table 7.3	Yearly direct discharges

| Field Name | Description | Type / Format |
| --- | --- | --- |
| CRY_CD | Country Code ISO3166 two digit country code, see Annex 6. | Text 2 chars |
| YEAR | Year Of aggregation period. | Integer |
| SEA_AREA_NAME_ID | Sea Area Name or ID Into which river discharges. | Text 50 chars |
| SEA_REGION_NAME | Regional Sea Name Of which Sea Area is a part of. | Text 50 chars |
| SEA_CONVENTION_AREA | Marine Convention Sea Area Name | Text 50 chars |
| Estimate | Estimate Lower estimate based on treating determinand values that are less than the limits of detection as zero. Upper estimate based on treating determinand values that are less than the limits of detection as values equivalent to the limit of detection value. | Number 4 decimal places |
| Nitrate | Nitrate Direct Discharges of Nitrate expressed in kilotonnes (kt). | Number 4 decimal places |
| Nitrite | Nitrite Direct Discharges of Nitrite: expressed in kilotonnes (kt). | Number 4 decimal places |
| Orthophosphate | Orthophosphate Direct Discharges of Orthophosphate: expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Nitrogen | Total Nitrogen Direct Discharges of Total Nitrogen expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Phosphorus | Total Phosphorus Direct Discharges of Total Phosphorus expressed in kilotonnes (kt). | Number 4 decimal places |
| Ammonia | Ammonia Direct Discharges of Ammonia expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Mercury | Total Mercury Direct Discharges of Total Mercury expressed in tonnes (t). | Number 4 decimal places |
| Total Cadmium | Total Cadmium Direct Discharges of Total Cadmium expressed in tonnes (t). | Number 4 decimal places |
| Total Zinc | Total Zinc Direct Discharges of Total Zinc expressed in tonnes (t). | Number 4 decimal places |
| Total Lead | Total Lead Direct Discharges of Total Lead expressed in tonnes (t). | Number 4 decimal places |
| Copper | Copper Direct Discharges of Copper expressed in tonnes (t). | Number 4 decimal places |
| Nickel | Nickel Direct Discharges of Nickel expressed in tonnes (t). | Number 4 decimal places |
| Chromium | Chromium Direct Discharges of Chromium expressed in tonnes (t). | Number 4 decimal places |
| Gamma-HCH | Gamma-HCH Direct Discharges of Gamma-HCH expressed in tonnes (t). | Number 4 decimal places |
| Suspended Particulate Matter | Suspended Particulate Matter Direct Discharges of Suspended Particulate Matter expressed in tonnes (t). | Number 4 decimal places |
| Hydrocarbons | Hydrocarbons Direct Discharges of Hydrocarbons expressed in kilotonnes (kt). | Number 4 decimal places |
| Detergents | Detergents Direct Discharges of Detergents expressed in kilotonnes (kt). | Number 4 decimal places |
| Phenols | Phenols Direct Discharges of Phenols expressed in kilotonnes (kt). | Number 4 decimal places |
| PCB-28 | PCB-28 Direct Discharges of PCB-28 expressed in tonnes (t). | Number 4 decimal places |
| PCB-52 | PCB-52 Direct Discharges of PCB-52 expressed in tonnes (t). | Number 4 decimal places |
| PCB-101 | PCB-101 Direct Discharges of PCB-101 expressed in tonnes (t). | Number 4 decimal places |
| PCB-118 | PCB-118 Direct Discharges of PCB-118 expressed in tonnes (t). | Number 4 decimal places |
| PCB-153 | PCB-153 Direct Discharges of PCB-153 expressed in tonnes (t). | Number 4 decimal places |
| PCB-138 | PCB-138 Direct Discharges of PCB-138 expressed in tonnes (t). | Number 4 decimal places |
| PCB-180 | PCB-180 Direct Discharges of PCB-180 expressed in tonnes (t). | Number 4 decimal places |
| Total PCBs | Total PCBs Direct Discharges of Total PCBs expressed in tonnes (t). | Number 4 decimal places |
| Other Hazardous Substances | Other Hazardous Substances Direct Discharges of Other Hazardous Substances expressed in tonnes (t). Provide name and CAS No of any additional hazardous substances monitored. | Number 4 decimal places |
| BOD-7 | BOD-7 Direct Discharges of BOD-7 expressed in kilotonnes (kt). | Number 4 decimal places |
| BOD-5 | BOD-5 Direct Discharges of BOD-5 expressed in kilotonnes (kt). | Number 4 decimal places |
| COD-Mn | COD-Mn Direct Discharges of COD-Mn expressed in kilotonnes (kt). | Number 4 decimal places |
| COD-Cr | COD-Cr Direct Discharges of COD-Cr expressed in kilotonnes (kt). | Number 4 decimal places |
| Total Organic Carbon | Total Organic Carbon Direct Discharges of Total Organic Carbon expressed in kilotonnes (kt). | Number 4 decimal places |
| Organic Compounds | Organic Compounds Direct Discharges of Organic Compounds expressed in kilotonnes (kt). | Number 4 decimal places |
| Tritium | Tritium Direct Discharges of Tritium expressed in Becquerels (Bq). | Number 4 decimal places |
| Radionuclides | Radionuclides Direct Discharges of Radionuclides expressed in Becquerels (Bq). Provide name of any additional radionuclides monitored. | Number 4 decimal places |
| Volume for the Year | Volume for the Year Expressed in cubic metres (m3). | Number 2 decimal places |
| Long Term Annual Discharge Volume | Long Term Annual Discharge Volume Expressed in cubic metres per second (m3/sec). | Number 2 decimal places |
| Remarks | Remarks Additional comments. | Text 100 chars |

# 8.	Delivery of Data Files

Preferably the supplied templates should be used for data exchange.

Data files for the EUROWATERNET Transitional, Coastal and Marine Water priority data flow should be uploaded to the national repository of your country.  This is the delivery point for all national data requested under EIONET priority data flows..

Your national repository is either your country’s folder in the Central Data Repository or a designated CIRCLE Interest Group on your national EIONET server.  This depends on the choice of your country for delivering EIONET priority data.  Please see the result of the repository choice on the EIONET portal.

If your country has opted for the Central Data Repository (CDR) EUROWATERNET data deliveries have to be uploaded to your country’s folder under EEA Requests.  The online Help (‘Help Area’ button) explains how to create new envelopes and upload data files.

If your country has chosen to deliver the EIONET priority data to the CIRCLE Interest Group on the national EIONET server, EUROWATERNET deliveries should be uploaded to the appropriate library sub-section.  Use the ‘File Upload’ button to upload the data files.

File upload permissions to country folders on the CDR or to the national CIRCLE Interest Group for data deliveries are organised by the National Focal Point (NFP).  Please contact your NFP if you have a question.

# 9.	Timetable

The data and information obtained through EUROWATERNET is required for the formulation of indicators that will be used in a number of EEA reports including:

- Environmental Signals

- Water Indicator Report

The annual schedule for the update of EUROWATERNET and for the production of factsheets for the above reports is outlined below.

|  | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Letter requesting data sent to NFPs | ( |  |  |  |  |  |  |  |  |  |
| EUROWATERNET update |  |  |  |  |  |  |  |  |  |  |
| Deadline for updated data from countries |  |  | ( |  |  |  |  |  |  |  |
| Inclusion of data into database and validation procedure |  |  |  |  |  |  |  |  |  |  |
| Draft fact sheets |  |  |  |  |  |  |  |  |  |  |
| NFP comments on factsheets |  |  |  |  |  |  |  |  |  |  |

MARINEBASE/Waterbase transitional, coastal, marine will be updated with the data collected through the EUROWATERNET process and will be used in the production of factsheets for upcoming reports.

For any further information on these guidelines or for technical assistance please contact Steve Nixon of the ETC/WTR Core Team, based at the Water Research Centre, Swindon, UK. Contact details below.

Steve Nixon

tel:	+44 1793 865166

fax:	+44 1793 865001

e-mail: 	nixon@wrcplc.co.uk

# 10.	References

Nixon, S., J. Grath, J. Bøgestrand, 1999. EUROWATERNET - The European Environment Agency's Monitoring and Information Network for Inland Water Resources - Technical Guidelines for Implementation. EEA Technical report No 7.

Nygaard, K., Rygg, B. and Bjerkeng, B., 2001. Marinebase — Database on aggregated data for the coastline of the Mediterranean, Atlantic, North Sea, Skagerrak, Kattegat and Baltic. EEA Technical report No 58.

Annex 1	Priority Substances identified by the Water Framework Directive, Lists I and II of the Dangerous Substances Directive and by the Marine Conventions

WFD_PS 	Water Framework Directive Priority Substance

WFD_PHS 	Water Framework Directive Priority Hazardous Substance

WFD_PSR 	Water Framework Directive Priority Substance under Review

DSD	Dangerous Substances Directive

HELCOM	Priority substances as listed by HELCOM

OSPAR		and OSPAR

| CAS No | Substance | WFD_PS | WFD_PHS | WFD_PSR | DSD | HELCOM | OSPAR |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Aliphatic Hydrocarbons |  |  |  |  |  |  |
| 4904-61-4 | 1,5,9 cyclododecatriene |  |  |  |  |  | ( |
| 294-62-2 | Cyclododecane |  |  |  |  |  | ( |
|  | Brominated diphenylethers |  | ( |  |  |  |  |
| 1163-19-5 | Bis(pentabromophenyl) ether |  |  |  |  |  |  |
| 32536-52-0 | Diphenyl ether, octabromo deviate |  |  |  |  |  |  |
| 32534-81-9 | Diphenyl ether, pentabromo derivative |  |  |  |  |  |  |
|  | Metallic Compounds |  |  |  |  |  |  |
| 7440-43-9 | Cadmium and its compounds |  | ( |  | ( | ( | ( |
| 7440-47-3 | Chromium and its compounds |  |  |  |  | ( | ( |
| 7440-50-8 | Copper and its compounds |  |  |  | ( |  |  |
| 7439-92-1 | Lead and its compounds |  |  | ( | ( | ( | ( |
| 7439-97-6 | Mercury and its compounds |  | ( |  | ( | ( | ( |
| 7440-02-0 | Nickel and its compounds | ( |  |  | ( |  |  |
| 7782-49-2 | Selenium and its compounds |  |  |  |  | ( |  |
| 7440-66-6 | Zinc and its compounds |  |  |  | ( |  |  |
|  | Organic Ester |  |  |  |  |  |  |
| 51000-52-3 | Neodecanoic acid, ethanyl ester |  |  |  |  |  | ( |
|  | Organic Nitrogen Compound |  |  |  |  |  |  |
| 55525-54-7 | 3,3’-(ureylenedimethylene)bis(3,5,5-trimethylcyclohexyl) diisocyanate |  |  |  |  |  |  |
| 793-24-8 | 4-(dimethylbutylamino) diphenylamin (6PPD) |  |  |  |  |  | ( |
|  | Organohalogens |  |  |  |  |  |  |
| 79-94-7 | Tetrabromobisphenol A (TBBP-A) |  |  |  |  |  | ( |
| 77-47-4 | Hexachlorocyclopentadiene (HCCP) |  |  |  |  |  | ( |
| 87-61-6 | (1,2,3-trichlorobenzene) |  |  | ( |  |  | ( |
| 120-82-1 | (1,2,4-trichlorobenzene) |  |  | ( |  |  | ( |
| 108-70-3 | (1,3,5-trichlorobenzene) |  |  | ( |  |  | ( |
| 85535-84-8 | C10-13-Chloralkanes |  | ( |  |  | ( | ( |
| 67-66-3 | Trichloromethane | ( |  |  | ( | ( |  |
| 85-22-3 | Pentabromoethylbenzene |  |  |  |  |  | ( |
| 2440-02-0 | Heptachloronorbornene |  |  |  |  |  | ( |
| 1825-21-4 | Pentachloroanisole |  |  |  |  |  | ( |
| 36065-30-2 | 2,4,6-bromophenyl 1-2(2,3-dibromo-2-methylpropyl) |  |  |  |  |  | ( |
|  | Polychlorinated naphthalenes: |  |  |  |  |  |  |
| 1321-65-9 | Trichloronaphthalene |  |  |  |  |  | ( |
| 1335-88-2 | Tetrachloronaphthalene |  |  |  |  |  | ( |
| 1321-64-8 | Pentachloronaphthalene |  |  |  |  |  | ( |
| 1335-87-1 | Hexachloronaphthalene |  |  |  |  |  | ( |
| 32241-08-0 | Heptachloronaphthalene |  |  |  |  |  | ( |
| 2234-13-1 | Octachloronaphthalene |  |  |  |  |  | ( |
| 70776-03-3 | Naphthalene, chloro derivatives |  |  | ( | ( |  | ( |
|  | Organophosphate |  |  |  |  |  |  |
| 603-35-0 | Triphenyl phosphine |  |  |  |  |  | ( |
|  | Organosilicane |  |  |  |  |  |  |
| 107-46-0 | Hexamethyldisiloxane (HMDS) |  |  |  |  |  | ( |
|  | Organotin Compounds |  |  |  |  |  |  |
| 36643-28-4 | (TBT-ion) |  | ( |  |  |  |  |
| 688-73-3 | Tributyltin compounds |  | ( |  | ( |  | ( |
|  | Pesticides and Biocides |  |  |  |  |  |  |
| 106-93-4 | 1,2-Dibromoethane |  |  |  |  | ( |  |
| 93-76-5 | 2,4,5-T |  |  |  |  | ( |  |
| 107-13-1 | Acrylonitrile |  |  |  |  | ( |  |
| 309-00-2 | Aldrin |  |  |  | ( | ( |  |
| 140-57-8 | Aramite |  |  |  |  | ( |  |
| 319-86-8 | beta-HCH |  |  |  |  | ( |  |
| 57-74-9 | Chlordane |  |  |  |  | ( |  |
| 1034-41-9 | Chlordecone (Kepone) |  |  |  |  | ( |  |
| 6164-98-3 | Chlordimeform |  |  |  |  | ( |  |
| 789-02-6 | DDT, o,p’ |  |  |  | ( | ( |  |
| 50-29-3 | DDT, p,p’ |  |  |  | ( | ( |  |
| 72-55-9 | DDE, p, p’ |  |  |  | ( |  |  |
| 72-54-8 | DDD, p, p’ |  |  |  | ( |  |  |
| 53-19-0 | DDD, o, p’ |  |  |  | ( |  |  |
| 60-57-1 | Dieldrin |  |  |  | ( | ( |  |
| 72-20-8 | Endrin |  |  |  | ( | ( |  |
| 144-49-0 | Fluoroacetic acid and derivatives |  |  |  |  | ( |  |
| 608-73-1 | Hexachlorocyclohexane |  | ( |  |  | ( | ( |
| 58-89-9 | (gamma-isomer, Lindane) |  | ( |  | ( | ( | ( |
| 76-44-8 | Heptachlor |  |  |  |  | ( |  |
| 118-74-1 | Hexachlorobenzene |  | ( |  | ( | ( |  |
| 297-78-9 | Isobenzane |  |  |  |  | ( |  |
| 465-73-6 | Isodrin |  |  |  | ( | ( | ( |
| 4234-79-1 | Kelevan |  |  |  |  | ( |  |
| 2385-85-5 | Mirex |  |  |  |  | ( |  |
| 4636-83-3 | Morfamquat |  |  |  |  | ( |  |
| 1836-75-5 | Nitrophen |  |  |  |  | ( |  |
| 87-86-5 | Pentachlorophenol |  |  | ( | ( | ( | ( |
| 82-68-8 | Quintozene |  |  |  |  | ( |  |
| 8001-35-2 | Toxaphene |  |  |  |  | ( |  |
| 115-32-2 | Dicofol |  |  |  |  |  | ( |
| 115-29-7 | Endosulfan |  |  | ( |  |  | ( |
| 959-98-8 | (alpha-Endosulfan) |  |  | ( | ( |  |  |
| 72-43-5 | Methoxychlor |  |  |  |  |  | ( |
| 1582-09-8 | Trifluralin |  |  | ( | ( |  | ( |
| 2104-64-5 | Ethyl O-(p-nitrophenyl) phenyl phosphonothionate (EPN) |  |  |  |  |  | ( |
| 70124-77-5 | Flucythrinate |  |  |  |  |  | ( |
| 2227-13-6 | Tetrasul |  |  |  |  |  |  |
|  | Pharmaceutical |  |  |  |  |  |  |
| 512-04-9 | Diosgenin |  |  |  |  |  | ( |
| 23593-75-1 | Clotrimazole |  |  |  |  |  | ( |
|  | Phenols |  |  |  |  |  | ( |
| 9016-45-9 | Nonylphenolethoxylate & degradation/transformation products |  |  |  |  | ( |  |
| 84852-15-3 | Nonylphenol, 4- |  |  |  |  | ( |  |
| 732-26-3 | 2,4,6-tri-tert-butylphenol |  |  |  |  |  | ( |
| 1806-26-4 | Octylphenols |  |  | ( |  |  |  |
| 140-66-9 | (para-tert-octylphenol) |  |  |  |  |  | ( |
| 25154-52-3 | Nonylphenols |  | ( |  |  |  |  |
| 104-40-5 | (4-(para)-nonylphenol) |  |  |  |  |  |  |
| 8452-15-3 | (4-nonylphenol, branched) |  |  |  |  |  |  |
|  | Phthalate Esters |  |  |  |  |  |  |
|  | Diethylhexylphthalate |  |  |  |  | ( |  |
| 84-74-2 | Dibutylphthalate |  |  | ( |  | ( |  |
| 117-81-7 | Di (2-ethylhexyl) phthalate (DEHP) |  |  | ( |  | ( |  |
| 84-66-2 | Di-ethyl phthalate |  |  | ( |  |  |  |
| 84-69-5 | Di-iso-butyl phthalate |  |  | ( |  |  |  |
| 85-68-7 | Butyl benzyl phthalate (BBP) |  |  | ( |  |  |  |
|  | Polycyclic Aromatic Hydrocarbons |  | ( |  |  | ( | ( |
| 50-32-8 | (benzo-a-pyrene) |  |  |  |  |  |  |
| 205-99-2 | (benzo-b-fluoranthene) |  |  |  |  |  |  |
| 191-24-2 | (benzo-g,h,i-perylene) |  |  |  |  |  |  |
| 207-08-9 | (benzo-k-fluoranthene ) |  |  |  |  |  |  |
| 206-44-0 | (fluoroanthene) |  |  |  |  |  |  |
| 193-39-5 | (indeno(1,2,3-cd) pyrene) |  |  |  |  |  |  |
| 98-51-1 | 4-tert-butyltoluene |  |  |  |  |  | ( |
|  | Polycyclic Halogenated Aromatic Compounds |  |  |  |  |  |  |
| 36355-01-8 | Hexabromobiphenyl |  |  |  |  | ( |  |
| 1336-36-3 | Polychlorinated biphenyls |  |  |  | ( | ( | ( |
| 7012-37-5 | 2,4,4'-trichlorobiphenyl (CB28) |  |  |  |  |  |  |
| 35693-99-3 | 2,2',5,5'-tetrachlorobiphenyl (CB52) |  |  |  |  |  |  |
| 32598-13-3 | 3,3’,4,4’-tetrachlorobiphenyl (CB77) |  |  |  | ( |  |  |
| 37680-73-2 | 2,2',4,5,5'-pentachlorobiphenyl (CB101) |  |  |  |  |  |  |
| 32598-14-4 | 2,3,3',4,4'-pentachlorobiphenyl (CB105) |  |  |  |  |  |  |
| 31508-00-6 | 2,3',4,4',5-pentachlorobiphenyl (CB118) |  |  |  | ( |  |  |
| 35065-28-2 | 2,2',3,4,4',5'-hexachlorobiphenyl (CB138) |  |  |  |  |  |  |
| 35065-27-1 | 2,2',4,4',5,5'-hexachlorobiphenyl (CB153) |  |  |  |  |  |  |
| 38380-08-4 | 2,3,3',4,4',5-hexachlorobiphenyl (CB156) |  |  |  |  |  |  |
| 32774-16-6 | 3,3',4,4',5,5' HexCB (PCB169) |  |  |  | ( |  |  |
| 35065-29-3 | 2,2',3,4,4',5,5'-heptachlorobiphenyl (CB180) |  |  |  |  |  |  |
| 2051-24-3 | 5,5',6,6'-decachlorobiphenyl (CB209) |  |  |  |  |  |  |
| 106-43-4 | PCT (mixtures) |  |  |  |  | ( |  |
| 1746-01-6 | TCDD (dioxins & furans) |  |  |  |  | ( |  |
|  | Brominated flame retardants |  |  |  |  |  | ( |
|  | Polychlorinated dibenzodioxins (PCDD) |  |  |  |  | ( | ( |
| 136677-10-6 | Polychlorinated dibenzofurans (PCDF) |  |  |  |  | ( | ( |
|  | Synthetic Musk |  |  |  |  |  |  |
| 81-15-2 | Musk xylene |  |  |  |  | ( | ( |
| 15972-60-8 | Alachlor | ( |  |  |  |  |  |
| 120-12-7 | Anthracene |  |  | ( | ( |  |  |
| 1912-24-9 | Atrazine |  |  | ( | ( |  |  |
| 71-43-2 | Benzene | ( |  |  | ( |  |  |
| 470-90-6 | Chlorfenvinphos | ( |  |  |  |  |  |
| 2921-88-2 | Chlorpyrifos |  |  | ( |  |  |  |
| 107-06-2 | 1,2-Dichloroethane | ( |  |  | ( |  |  |
| 75-09-2 | Dichloromethane | ( |  |  | ( |  |  |
| 919-86-8 | Demeton-S-methyl |  |  |  | ( |  |  |
| 62-73-7 | Dichlorvos |  |  |  | ( |  |  |
| 60-51-5 | Dimethoate |  |  |  | ( |  |  |
| 330-54-1 | Diuron | ( |  |  |  |  |  |
| 87-68-3 | Hexachlorobutadiene |  | ( |  | ( |  |  |
| 34123-59-6 | Isoproturon | ( |  |  |  |  |  |
| 330-55-2 | Linuron |  |  |  | ( |  |  |
| 608-93-5 | Pentachlorobenzene |  | ( |  |  |  |  |
| 122-34-9 | Simazine | ( |  |  | ( |  |  |
| 12002-48-1 | Trichlorobenzenes |  |  | ( | ( |  |  |

Annex 2	Physico-chemical determinands required for chemical quality

| Determinand | Abbreviation | Unit | Water Body1 |
| --- | --- | --- | --- |
| BOD5 | BOD5 | µMol O2 | T |
| BOD7 | BOD7 | µMol O2 | T |
| Chlorophyll a | Chl-a | µg/l | T, C, M |
| COD | COD | µMol O2 | T |
| Dissolved Oxygen2 | O2 | µMol O2 | T, C, M |
| Nitrate | NO3 -N | µMol N | T, C, M |
| Nitrate to Orthophosphate ratio | NO3 /PO4 | Molar ratio | T, C, M |
| Organic Nitrogen | mg/l N | µMol N | T, C, M |
| Orthophosphate | PO4 –P | µMol P | T, C, M |
| Oxygen Saturation2 | O2 | % | T, C, M |
| Silicate | SiO3 -Si | µMol Si | T, C, M |
| Total Ammonium | NH4 -N | µMol N | T, C, M |
| Total Nitrogen | TOT-N | µMol N | T, C, M |
| Total Nitrogen to Total Phosphorus ratio | TOT-N /TOT-P | Molar ratio | T, C, M |
| Total Organic Carbon | TOC | µMol C | T |
| Total Oxidised Nitrogen | NO3 -N + NO2 -N | µMol N | T, C, M |
| Total Phosphorus | TOT-P | µMol P | T, C, M |

1  Water Body:

T = Transitional water

C = Coastal water

M = Marine water

2  Particularly in relation to measuring and detecting low oxygen concentrations in         	bottom layers of water.

Annex 4	Species Codes used in sampling of biota

Biota data should use the Species Codes detailed in this list, based on the ICES coding method of the first four characters of the genus name followed by a space and the first three characters of the species name.  The primary list is based on the recommended species for the different Marine Conventions.  Please also include data for other species that are included in long-term monitoring programmes,  using the same coding convention as detailed above.

| Species Code | Systematic Name | English Name | MC1 |
| --- | --- | --- | --- |
| ARIS ANT | Aristeus antennatus | Blue and red shrimp | M |
| BOOP BOO | Boops boops | Bogue | M |
| CLUP HAR | Clupea harengus | Atlantic herring | B |
| CRAS GIG | Crassostrea gigas | Giant cupped oyster | O |
| GADU MOR | Gadus morhua | Atlantic cod | B, O |
| FUCU VES | Fucus vesiculosis | Bladder wrack | B |
| LIMA LIM | Limanda limanda | Common dab | O |
| MACO BAL | Macoma balthica | Baltic tellin | B |
| MERL MCC | Merluccius merluccius | European hake | M, O |
| MERL MNG | Merlangius merlangus | Whiting | O |
| MULL BAR | Mullus barbatus | Red mullet | M |
| MULL SUR | Mullus surmuletus | Striped red mullet | M |
| MYTI EDU | Mytilus edulis | Common mussel | B, O |
| MYTI GAL | Mytilus galloprovincialis | Mediterranean mussel | M |
| NEPH NOR | Nephrops norvegicus | Norway lobster | M, O |
| PERC FLU | Perca fluviatilis | Perch | B |
| PLAT FLE | Platichthys flesus | European flounder | B, O |
| SADU ENT | Saduria entomon |  | B |
| THUN THY | Thunnus thynnus | Northern bluefin tuna | M |
| ZOAR VIV | Zoarces viviparus | Vivparous blenny | B |

1  MC 	Marine Convention

B = Baltic, HELCOM Combine programme

M =Mediterranean MAP

O = OSPAR, JAMP

Annex 5	Tissue Codes used in sampling 			of biota

Biota data should be reported using the Tissue Codes in this list.

| Tissue Code | English Name |
| --- | --- |
| LI | Liver |
| MU | Muscle |
| SB | Soft parts (homogenised whole body without carapace or shell) |
| WO | Whole body |

Annex 6	Selected ISO Country codes

The Country Code should be reported using the ISO 3166 A2 codes in this list.

| Official name of country | ISO A2 |
| --- | --- |
| Albania | AL |
| Armenia | AM |
| Austria | AT |
| Azerbaijan | AZ |
| Belarus | BY |
| Belgium | BE |
| Bosnia and Herzegovina | BA |
| Bulgaria | BG |
| Croatia | HR |
| Cyprus | CY |
| Czech Republic | CZ |
| Denmark | DK |
| Estonia | EE |
| Finland | FI |
| France | FR |
| Georgia | GE |
| Germany | DE |
| Gibraltar | GI |
| Great Britain | GB |
| Greece | GR |
| Hungary | HU |
| Iceland | IS |
| Ireland | IE |
| Italy | IT |
| Kazakstan | KZ |
| Kyrgyzstan | KG |
| Latvia | LV |
| Liechtenstein | LI |
| Lithuania | LT |
| Luxembourg | LU |
| Macedonia, the Former Yugoslav Republic of | MK |
| Malta | MT |
| Moldova, Republic of | MD |
| Netherlands | NL |
| Norway | NO |
| Poland | PL |
| Portugal | PT |
| Romania | RO |
| Russian Federation | RU |
| Slovakia | SK |
| Slovenia | SI |
| Spain | ES |
| Sweden | SE |
| Switzerland | CH |
| Tajikistan | TJ |
| Turkey | TR |
| Turkmenistan | TM |
| Ukraine | UA |
| Uzbekistan | UZ |
| Yugoslavia | YU |

# Footnotes

Harmonised selection methodology and criteria for representative stations in transitional waters, including for example the salinity question for nutrients and other dissolved substances, will be crucial. Guidelines are available from Marine Conventions or ICES.

2 These are as follows: phenanthrene, anthracene, fluoranthene, pyrene, benzo[a]anthracene, chrysene, benzo[a]pyrene, benzo[ghi]perylene, indeno[1,2,3-cd]pyrene.

3 Provided that a suitable method is available.