Report concerning Art. 10 of the EU's Nitrate Directive

2002 report

The EU's Nitrate Directive dates from 1991, but has been in force in Iceland since 1994.

Cultivation and nitrogen fertilizer use in Iceland, general comments

Iceland covers an area of 103,000 km2, including cultivated fields that amount to only ca. 1,400 km2 (136,000 ha). Most of these are hayfields. It is estimated that only 70 km2 are used for other cultivation, i.e. for potatoes, barley, etc., and are left with bare soil in autumn and winter

In 1980, the use of artificial chemical nitrogen fertilizer reached a maximum of about 15,000 tons per year. Since then, the use of nitrogen fertilizers has been reduced and is currently (2000) 12,681 tons per year. In 1999, 2.200 tons of Phosphorus was used as fertilizer. It has been estimated that ca. 2,000 tones of nitrogen are spread on cultivated fields annually in the form of animal manure. This is equivalent to 15 kg N/ha. Thus, the total N-balance is c. 110 kg N/ha for cultivated land. Considering that cultivated areas constitute only 1.4% of the country's total area, low population density, and high annual precipitation, averaging 2,000 mm per year (with local variations ranging from 400 to 4,000 mm) - polluted waters according to the definitions in the directive, and vulnerable zones, are not likely to be encountered.

Information to be contained in reports concerning Article 10

Following information is requested to be in the report

1. A statement of the preventive action taken pursuant to Article 4, which covers the preparation of instructions on sound working practices in agriculture:

A code of good agricultural practice with recommendations to farmers on sound working practices in agriculture regarding the use of fertilizers has been made and is available on The Environment and Food Agency’s homepage (http:// www.ust.is).

2. A map showing the following:

a) Waters identified in accordance with Article 3 (1) and Annex I indicating for each water which of the criteria in Annex I was used for the purpose of identification.

In Iceland no such waters are to be found

b) The location of the defined vulnerable zones, distinguishing between existing zones and zones designated since the previous report.

In Iceland no such areas are to be found.

3. A summary of the monitoring results obtained pursuant to Article 6, including a statement of the considerations which led to the designation of each vulnerable zone and to any revision of or addition to designations of vulnerable zones.

See the enclosed report describing the situation regarding nitrates in water in Iceland.

4. A summary of the action programmes drawn up pursuant to Article 5 and, in particular:

a) the measures required by Article 5 (4) (a) and (b);

b) the information required by Annex III (4);

c) any additional measures or reinforced actions taken pursuant to Article 5 (5);

d) a summary of the results of the monitoring programmes implemented pursuant to Article 5 (6);

e) the assumptions made by the Member States  about the likely time scale within which the waters identified in accordance with Article 3 (1) are expected to respond to the measures in the action programme, along with an indication of the level of uncertainty incorporated in these assumptions.

This item covers the action taken in areas, which have been defined as vulnerable. No such areas are to be found in Iceland, so this item does not apply as far as Iceland is concerned.

Summary on the implementation of EU directive No. 91/676 on the protection of waters against nitrate pollution from agriculture in Iceland, especially as concerns Art. 6, items (a), (b) and (c).

2002 report

I.	Introduction

The EU's directive No. 91/676 on the protection against nitrate pollution from agriculture is now incorporated into Icelandic law with the Regulation no. 804/1999 on water protection against nitrogen pollution from agriculture and other sources. According to this Regulation, local boards of health are to define and submit to the Environment and Food Agency information about the areas that are vulnerable regarding eutrophication. Then a list of these areas is to be issued and the areas monitored as applicable. Such mapping is to be repeated every 4 years or every eight years if the concentration of nitrates is below 25 milligrammes per litre. Today, the Environment and Food Agency is aware of only a very few sea lagoons with a sandbar at the outlet, a salt-covered bottom and a fresh surface layer which could be covered by the definition of the directive on vulnerable areas. Fluctuations in the natural inflow of the sea are considered to have greater effect on the condition of such waters as regards nutrient and oxygen content rather than effluents from agriculture. It is unlikely that other areas are to be found in Iceland, which could be defined as vulnerable on the basis of the definition in the directive and no local board of health have yet found it relevant to define vulnerable areas in regard to eutrophication. However, it is possible that areas may be found which it is desirable to protect in the long run against the polluting effluents, especially nitrogen, to protect fishing-rights interests and special ecosystems, i.a. to protect the diversity of species and ecosystems.

II.	Summary of available data

1.	Drinking water and springs

Article 6 (a) of the EU directive covers the mapping (taking of samples and measurements) of the nitrate concentration of surface water and ground water used as drinking water.

Environment and Food Agency have in database results of ca 161 analyses of drinking water (spring water, well water and surface water) sampled in 1999, 2000 and 2001. All these measurements show that the nitrate nitrogen concentration in water used as drinking water in Iceland is under 1,4 mg/l-N, or less than 6,2 mg/l nitrate, which is well under 25 milligrammes per litre. All exept one measurement are under 0,5 mg/l-N, or less than 2,2 mg/l nitrate.

The largest reservoirs of these are at the Reykjavik Metropolitan Area. The principal water reservoir of the City of Reykjavik (Gvendarbrunnar). The water flow from this reservoir is about 1 m3 per second and it is used as drinking water by roughly 40-50% of the nation.

About 95% of Iceland's drinking water is extracted from springs. Surface water constitutes about 5% of Iceland's drinking water. Surface water used for drinking is obtained from mountain lakes, which are not subject to any nitrate effects, and from river basins.

A. Lakes

The nutrient status of 39 lakes was measured in the fall 1997 and 1998. This was the first attempt that has ever been made to categorize lakes with respect to their nutrient status or nutrient production, as hypertrophy of lakes is an unknown phenomenon in Iceland. Of total 59 lakes measured in the period 1997 to 2000, 49 lakes had nitrate nitrogen concentrations (NO3-N) less than 0,005 mg/l and all the lakes had nitrate nitrogen concentrations less than 0,05 mg/l.

For Total Nitrogen:

Total N		Number of lakes

<0,3 mg/l 		52 lakes

0,3 - 0,75 mg/l	 5 lakes

0,75 - 1,5 mg/l	 2 lakes

For Total Phosphorus:

Total P			Number of lakes

<0,01 mg/l		36 lakes

0,010 - 0,025 mg/l	12 lakes

0,025 - 0,050 mg/l	4 lakes

0,050 - 0,125 mg/l	7 lakes

Part of these results and other data are discussed in more detail in report published in 1999 by Assessment and Monitoring Committee (AMSUM) under The Ministry for the Environment.

B.	Rivers

A fair survey of the nitrate concentration in the country's principal rivers were available (Unnsteinn Stefánsson, Jón Ólafsson, 1991). The average nitrate concentration in Icelandic rivers was estimated as about 0.17 mg/l of nitrate. Water for chemical analysis were sampled monthly at four sampling points in South Icelandic rivers from December 1998 to January 2002 and seven sampling points in East Icelandic rivers from November 1998 to November 2001. Nutrients and metals were analysed. The ranges in South Iceland, for nitrate nitrogen were between <0,002 to 0,055 mg N/l (<0,009-0,24 mg/l Nitrate) and for Phosphate 0,00 to 0,055 mg P/l respectively. The ranges in East Iceland, for nitrate nitrogen were between <0,002 to 0,124 mg N/l (<0,009-0,55 mg/l Nitrate) and for Phosphate 0,002 to 0,081 mg P/l respectively.

3. Coastal waters and estuaries

A. Coastal waters

The Marine Research Institute performs measurements of nitrate concentrations in the ocean surface at least twice a year, and the highest concentration quoted is about 0.75 mg/l nitrate. Coastal values reported pby Assessment and Monitoring Committee (AMSUM) in 1999 are lower. Stefánsson and Ólafsson's article (1991) shows that the average concentration of nitrates in river water carried to the sea in Iceland is only a third of the natural nitrate concentration of the ocean (winter value). Therefore, nitrates carried by river water to the ocean cannot in any way influence the nutrient status of the ocean around Iceland. The Marine Research Institute also performs measurements on chlorophyll-a.

The nutritional status in the main water masses is shown in table 1.

Table 1. The mean concentration of phosphate and nitrate in the Atlantic water masses and Arctic water masses in February-March 1991 (1,2) in Icelandic waters.

|  | Number of samples | PO4-P | NO3-N |
| --- | --- | --- | --- |
|  |  | µmol/l | µmol/l |
| Atlantic water | 31 | 0.95 | 13.9 |
| Arctic water | 30 | 0.87 | 12.9 |

In figure 2 concentrations of NO3-N and PO4-P in coastal currents are compared with the average concentrations in Atlantic and Arctic Waters (Ocean). The comparison clearly shows that the run-off from the country does not add to the nutritional load in the maritime area around Iceland.

Fig 2	.  Concentrations of nitrate and phosphate in coastal waters around Iceland

Further study of the concentrations of nutrients, both in solution and in suspended solids, in the vicinity of the sewage outlet in Reykjavik (fig 3) reveal slight changes in the concentrations of Si and in salinity  (fig 3 B and C).  Similar change, as found in Si concentrations was found for ammonia but not for other dissolved nutrients.

Elevated concentrations of nitrogen in suspended solids are found at the station nearest land (station 12) and station 6 (fig 3 D). The former is directly linked to the sewage outlet but the latter is most probably caused by resuspension of sediment. Similar profile is found for phosphorous in suspended solids.

Figure 3.	Measurements of some parameters in the seawater at Ánanaust 1995.

A) Stations, B) Concentrations of Si, C) Salinity and D) Concentrations of N in suspended matter.

Based on these results it is concluded that the coastal area around Iceland is a non-problem area regarding eutrophication and will be monitored according to that. In future, local authorities will be obliged to monitor the condition of the recipients of the effluents carried by their sewers. Thus, in future it should also be possible to obtain more data on the quantity of nutrients in coastal waters and in the vicinity of built-up areas.

B.	Estuaries

No comprehensive measurements of nitrates in estuaries are available. In the above-mentioned article by Stefánsson and Ólafsson the average concentration of nitrates in rivers by regions is calculated. The results for rivers in 1998-2002 indicate very low values.

# 4. References

Davíð Egilson, Elísabet D. Ólafsdóttir, Eva Yngvadóttir, Helga Halldórsdóttir, Flosi Hrafn Sigurðsson, Gunnar Steinn Jónsson, Helgi Jensson, Karl Gunnarsson, Sigurður Á Þráinsson, Andri Stefánsson, Hallgrímur Daði Indriðason, Hreinn Hjartarson, Jóhanna Margrét Thorlacius, Kristín Ólafsdóttir, Sigurður R Gíslason & Jörundur Svavarsson. March 1999. Levels of contaminants in the Icelandic environment (in Icelandic) 138 pp. Report published by Assessment and Monitoring Committee (AMSUM) under The Ministry for the Environment. Publised in March 1999

Unnsteinn Stefánsson & Jón Ólafsson, 1991.  Nutrients and fertility of Icelandic waters. Rit fiskideildar 12, 1-56

Jón Ólafsson, Magnús Danielsen, Sólveig Ólafsdóttir & Þórarinn Arnarson, 1996. Nutrients in seawater at Ánanaust November 1995 (in Icelandic). Hafrannsóknastofnun fjölrit nr. 50, 27 pp

Sigurður Reynir Gíslason, Árni Snorrason, Eydís Salome Eiríksdóttir, Bergur Sigfússon, Sverrir Óskar Elefsen, Jórunn Harðardóttir, Ásgeir Gunnarsson og Peter Torssander. Efnasamsetning, rennsli og aurburður straumvatna á Suðurlandi V. Gagnagrunnur Raunvísindastofnunar og Orkustofnunar. RH-12-2002.

Sigurður Reynir Gíslason, Árni Snorrason, Eydís Salome Eiríksdóttir, Bergur Sigfússon, Sverrir Óskar Elefsen, Jórunn Harðardóttir, Ásgeir Gunnarsson, Einar Örn Hreinsson, Peter Torssander, Marin I. Kardjilov og Níels Örn Óskarsson. Efnasamsetning, rennsli og aurburður straumvatna á Austurlandi III. Gagnagrunnur Raunvísindastofnunar og Orkustofnunar. RH-11-2002.

Data for nitrate concentrations in drinking water and lakes have been prepared by the Environmental and Food Agency.

Þættir úr Vistfræði Sjávar 1995. Hafrannsóknarstofnun fjölrit 44 (Marine Research Institute report no. 44)

Þættir úr Vistfræði Sjávar 1996. Hafrannsóknarstofnun fjölrit 53 (Marine Research Institute report no. 53)