Checking rules

TCM data

Jørgen Nørrevang Jensen

ICES

Introduction:

This document provides and overview of the data checking in relation to the EIONET TCM data. Some of these checks have been performed during spring-summer 2007 and the errors and “strange” data have been compiled in the attached document (Errors and “strange” data in the ETC TCM Database – updated with the most recent checks). Based on this list questions to the specific countries have been formulated and uploaded on CIRCA for further actions by EEA. Further checks have/are under development (those in bold).

The various checks are listed below in detail. It should be emphasised that these checks are based on the last years check performed by the former topic centre. In stead on repeating last years checks which showed a relatively small number or errors, some new checks have been developed in order to supplement these checks. The focus has been on the most important fields (e.g. information on fat weight and dry weight that is important for conversions of measurements made on different basis) but it should be emphasised that this is a system under development during the coming year.

It should be noted that the source of data to the ETC TCM database is several but can be separated into three categories:

- Data from the ICES Data Centre (data from the various commissions, OSPAR, HELCOM, AMAP etc). Between 0 and 98 % of the data enters via this source dependent on datatype;

- Data submitted through the EIONET system (data from national submissions). These data are in general structured in a specific way.

- Data in a different format than specified in the EIONET system. As an example ICES has received a copy of the UNEP/MAP database. The possibility to include these data will be investigated

Data entered through the ICES Data Centre has been through various screening procedures (dependent on datatype) before they are entered into the ETC TCM database. This does not mean that data trough this source is without errors but the types of errors might differ and the ways they are treated are dependent on the source.

Logical errors:

| Rule | Datatypes |
| --- | --- |
| 1. Day has to be integer from 1 to 31. (0 allowed if information on actual day is missing) | Hazardous substances in seawater, sediment, and biota. Nutrients in seawater Physical characteristics of stations |
| 2. Month has to be an integer from 1 to 12. (0 allowed if information on actual month is missing) | Hazardous substances in seawater, sediment, and biota. Nutrients in seawater Physical characteristics of stations |
| 3. Year cannot be larger than present year-1 | Hazardous substances in seawater, sediment, and biota. Nutrients in seawater Physical characteristics of stations |
| 4. Concentrations/loads has to be filled in. If the relevant determinand has not been measured no info should submitted. | Hazardous substances in seawater, sediment, and biota. Nutrients in seawater Riverine inputs Direct discharges |
| 5. Concentrations cannot be <= 0. Negative values and 0 should not be supplied | Hazardous substances in seawater, sediment, and biota. Nutrients in seawater Physical characteristics of stations |
| 6. Basis should be filled in with the codes D, L, or W | Hazardous substances in seawater, sediment, and biota. |
| 7. Tissue should be filled in with the codes LI, MU, SB, or WO. | Hazardous substances in biota. |
| 8. Fat Content cannot be larger than Dry wet ratio. | Hazardous substances in biota. |
| 9. SamplingDepth should not be larger than SeaDepth. Due to the fact that sampling depth can be larger than the “default” depth of the station the rule has been adjusted slightly: SeaDepth > 0.7*SamplingDepth | Hazardous substances in seawater, sediment, and biota. Nutrients in seawater Physical characteristics of stations |
| 10. SeaDepth should be checked for consistency with bathymetric maps. A checking routine will be developed for this check | Physical characteristics of stations |

Range checks:

| Check | Datatypes |
| --- | --- |
| 1. Latitude should lie between 30 and 90 degree North | Physical characteristics of stations |
| 2. Longitude should lie between 45 degree West and 43 degree East | Physical characteristics of stations |
| 3. Salinity above 45 per mille occurs very rarely unless sampling takes place very saline area like e.g. Mediterranean Salinas. Salinity (Nutrients in Seawater) should not be larger than salinity maximum (Physical Characteristics of Stations) | Nutrients in seawater Physical characteristics of stations |
| 4. The data in data table Nutrient in Seawater should lie within the limits set by Johnson et.al. (2006). Regional ranges are set for temperature, salinity, oxygen, phosphate, silicate, nitrate, pH, chlorophyll, and alkalinity. These ranges are in general quite broad but provide a good basis for a basic screening. | Nutrients in seawater |
| 5. Based on the ranges of concentrations in the ICES Data Centre data in the TCM database should be screened. Values to be questioned could be values less than (10 percentile/2) and values larger than (2* 90 percentile). | Hazardous substances in seawater, sediment, and biota. |

References:

Johnson, D.R., T.P. Boyer, H.E. Garcia, R.A. Locarnini, A.V. Mishonov, M.T. Pitcher, O.K. Baranova, J.I. Antonov, and I.V. Smolyar, 2006. World Ocean Database 2005 Documentation. Ed. Sydney Levitus. NODC Internal Report 18, U.S. Government Printing Office, Washington, D.C., 163 pp, Available at http: //www.nodc.noaa.gov/OC5/WOD05/docwod05.html.

| Errors and "strange" data in the ETC TCM Database |  |  |  |
| --- | --- | --- | --- |
| Table | Column | Type of error /Strange value | Country- code | Year | National- StationID | ImportRow | Determinand | Comment |
| TCM_NutrientsSeawater | Day | 0 | RO | 2001, 2002 |  |  |  |  |
| TCM_NutrientsSeawater | Day | 0 | SE | 1997-2002 |  |  |  |  |
| TCM_NutrientsSeawater | Day | 0 | MT | 2005 |  |  |  |  |
| TCM_NutrientsSeawater | Day | 0 | HR | 1998-2004 |  |  |  |  |
| TCM_NutrientsSeawater | Day | 0 | GR | 2000-2003 |  |  |  |  |
| TCM_NutrientsSeawater | Year | >2006 | SE | 2009, 2010 | GBSF17 |  |  |  |
| TCM_NutrientsSeawater | Concentrations | missing | GR | 2005 | GR_TCM_UNEP_GRE9_6 GR_TCM_UNEP_GRE5_4 |  | Orthophosphate Total Nitrogen |  |
| TCM_NutrientsSeawater | Concentrations | missing | EE | 2005 | K2 |  | Nitrate |  |
| TCM_NutrientsSeawater | Concentration | missing | BG | 2005 |  |  | CODMn Nitrate BOD5 Oxygen Saturation |  |
| TCM_NutrientsSeawater | Concentrations | missing | BE | 1999, 2002, 2003 | 154100 168900 |  | Total Phosphorus Total Organic Carbon Biological Oxygen Demand Chemical Oxygen Demand Ammonium |  |
| TCM_NutrientsSeawater | Concentrations | <0 without Limit OfDetection Flag filled in | EE | 2005 |  |  | Chlorophyll a |  |
| TCM_NutrientsSeawater | Concentrations | <0 without Limit OfDetection Flag filled in | PL | 2003 | K2 | 6260 | Total Organic Nitrogen |  |
| TCM_NutrientsSeawater | SampleDepth | missing | GR | 2005 | GR_TCM_UNEP_GRE6_3 |  |  |  |
| TCM_NutrientsSeawater | SampleDepth | missing | AL | 2004 |  |  |  |  |
| TCM_NutrientsSeawater | Salinity | >45 | SE | 2003 | GBBF13 |  |  |  |
| TCM_NutrientsSeawater | Salinity | >45 | FR | 2004, 2005 |  |  |  |  |
| TCM_NutrientsSeawater | Salinity | >45 | MT | 2003 |  |  |  |  |
| StationEIONETClassified | Latitude | < 33 | RO | 2005 |  |  |  | Latitude and Longitude swopped ? |
| TCM_ICES_ Hydrochemistry_ EWN_format | Day | missing | BE | 1986 |  |  |  |  |
| TCM_ICES_ Hydrochemistry_ EWN_format | Concentration | missing | PL,IE,NL, DK,DE,EE FR,FI,ES, SE,NO,GB, LV,PT |  |  |  | Total Oxidised Nitrogen |  |
| TCM_Hazardous SubstanceiBiota | Day | 0 | SE | 2001, 2003 |  |  |  |  |
| TCM_Hazardous SubstanceiBiota | Day | 0 | LV | 2001 |  |  |  |  |
| TCM_Hazardous SubstanceiBiota | Month | 0 | SE | 2001, 2003 |  |  |  |  |
| TCM_Hazardous SubstanceiBiota | Concentration | missing | TR | 2003 |  |  | Dissolved Oxygen | Should not be in this table |
| TCM_Hazardous SubstanceiBiota | Concentration | 0 without Limit OfDetection Flag filled in | RO, SE | 2005 |  |  |  |  |
| TCM_Hazardous SubstanceiBiotaICES | Day | 0 | GB,BE, SE, NL,IS | several |  |  |  |  |
| TCM_Hazardous SubstanceiBiotaICES | Concentration | extreme value 7.0 *(10)+12 | BE | 1993 |  | 141578 | Copper |  |
| TCM_Hazardous SubstanceiBiotaICES | DryWetRatio/Fat | Fat > DryWetRatio | NO | 1991,1997 1987,1996 2003 |  |  |  | Fat an order of magnitude to high ? |
| TCM_Hazardous SubstanceiBiotaICES | DryWetRatio/Fat | Fat > DryWetRatio | PL | 1989 1990 |  |  |  | Fat an order of magnitude to high ? |
| TCM_Hazardous SubstanceSediment | Day | 0 | MT | 2005 |  |  |  |  |
| TCM_Hazardous SubstanceSediment | Concentration | 0 without Limit OfDetection Flag filled in | RO | 2005 |  |  |  |  |
| TCM_Hazardous SubstanceSediment | Concentration | 0 without Limit OfDetection Flag filled in | PL | 2002 |  |  |  |  |
| TCM_Hazardous SubstanceSediment | BottomDepth | missing | HR | 1996-1998 | OT1 |  |  |  |
| TCM_Hazardous SubstanceSediment | Basis | X | MT, RO | 2005 |  |  |  |  |
| TCM_Hazardous SubstanceSedimentICES | Day | 0 | DE | 1986-1991 |  |  |  |  |
| TCM_Hazardous SubstanceSedimentICES | Day | 0 | GB | 1986-1988 |  |  |  |  |
| TCM_Hazardous SubstanceSedimentICES | Day | 0 | NL | 1985 |  |  |  |  |
| TCM_Hazardous SubstanceSedimentICES | Day | 0 | BE | 1988 |  |  |  |  |
| TCM_Hazardous SubstanceSedimentICES | Day | 0 | SE | 1990 |  |  |  |  |
| TCM_Hazardous SubstanceSedimentICES | Concentration and Unit | missing | DE,NO DK, GB | several |  |  | Total Nitrogen | Should this be in this table? |
| TCM_Hazardous SubstanceSedimentICES | Concentration and Unit | missing | DE, DK | several |  |  | Silicate | Should this be in this table? |
| TCM_Hazardous SubstanceSedimentICES | Concentration and Unit | missing | NL | several |  |  | pH | Should this be in this table? |
| TCM_Hazardous SubstanceSedimentICES | Concentration | 0 without Limit OfDetection Flag filled in | NL | 1990 |  |  |  |  |
| TCM_Hazardous SubstanceSeawater | Day | 0 | MT | 2005 |  |  |  |  |
| TCM_Hazardous SubstanceSeawater | Day | 0 | RO | 2001 2002 |  |  |  |  |
| TCM_Hazardous SubstanceSeawater | Day | 0 | SE | 1997-2000 |  |  |  |  |
| TCM_Hazardous SubstanceSeawater | Concentration | 0 without Limit OfDetection Flag filled in | RO | 2005 |  |  |  |  |
| TCM_RiverineInputs | Load | missing | FR | 1980- |  |  | Nitrite |  |
| TCM_RiverineInputs | Load | missing | LV | 2002 |  |  | Nitrite |  |
| TCM_RiverineInputs | Load | missing | BG | 2000-2002 |  |  | Nitrite |  |
| TCM_RiverineInputs | Load | missing | SI | 2005 |  |  | Various |  |
| StationEIONETClassified | WaterDepth | Waterdepth < (sampledepth)*0.7 | GR | 2004-2005 | UNEP_GRE3_IER UNEP_GRE3_KAV3 UNEP_GRE3_NES1 UNEP_GRE3_PIE1 UNEP_GRE3_STR1 UNEP_GRE3_STR3 UNEP_GRE3_STR4 UNEP_GRE3_THE2 UNEP_GRE3_THE5 |  |  | Questions to national sub- mitters not sent out jet |
| StationEIONETClassified | WaterDepth | Waterdepth < (sampledepth)*0.7 | HR | 1998-2005 | OC10 OC13 OC2 OC3 OC6 OC7 |  |  | Questions to national sub- mitters not sent out jet |
| StationEIONETClassified | WaterDepth | Waterdepth < (sampledepth)*0.7 | LT | 1995, 1998-2005 | 1 3 4 |  |  | Questions to national sub- mitters not sent out jet |
| StationEIONETClassified | WaterDepth | Waterdepth < (sampledepth)*0.7 | SE | 2002-2003 | B3 BPNO11 |  |  | Questions to national sub- mitters not sent out jet |

The rows in yellow are errors in relation to data coming via the ICES Data Centre and these will be handled by the ICES Data Centre.