## Slide 1
Nutrients and oxygen consuming substances in freshwater in Europe
Kari Austnes, Lidija Globevnik, Gašper Šubelj, Anne Lyche Solheim, Webinar on WISE-6, 29.09.2022

## Slide 2
Overview
Indicators CSI019 and CSI020
  New format and latest update
Technical issues
WISE-6 biological data

## Slide 3
The CSI019 and 020 indicators
CSI019: Oxygen consuming substances in European rivers
CSI020: Nutrients in freshwater in Europe
Large inputs of nutrients or organic pollutants can lead to eutrophication or de-oxygenation
Negative ecological impacts: Changes in species composition, species loss
Negative impacts on the use of water: Drinking, bathing, recreation
Main sources: Waste water and agriculture
Objective of several directives: WFD, UWWTD, DWD, ND
Trends: Are conditions improving?
Current status: Where do we see the largest problems now?

## Slide 4
Time series: oxygen consuming substances
All sites with time series from 1992 or 2000 and gaps < 3 years
Notes: Marked decrease, then apparent stabilisation

## Slide 5
Time series: nutrients
Notes: SW: Apparent stabilisation in recent years, especially for rivers
GW: Similar numbers of increasing and decreasing trends. 2018 peak due to FR

## Slide 6
Current status
All sites with data in 2018-2020: Far more sites than for time series
Concentration classes not mainly linked to policies: Objective to show distribution and compare
Notes: 3 mg O2/l: Fish Directive
11.3 mg NO3-N/l: ND/DWD – corresponds to 50 mg NO3/l

## Slide 7
New format EEA indicators
Short and concise
  Two plots: Aggregated (Europe) and disaggregated (country)
  Brief descriptive text and supplementary information
  No possibility to show country time series
First version 2022
  Time series for all determinands
  Current status plot only for one determinand
  Limited information on trend statistics
Notes: https://www.eea.europa.eu/ims/nutrients-in-freshwater-in-europe
https://www.eea.europa.eu/ims/oxygen-consuming-substances-in-european-rivers

## Slide 8
Further improvements
Technical improvements to existing indicator
  Links to current status plots for the other determinands
  Links to statistical tables
  Separate document with more detailed methodology descriptions
Notes: Depending on further developments

## Slide 9
Further improvements
Improved analyses
  More advanced statistical treatment of time series data
    Make full use of the reported data – far better spatial coverage
  Concentration classes in current status plots based purely on distribution (e.g. quintiles)
    Avoid misinterpretation
1992
2020
Notes: The intention is to work on this in 2023

## Slide 10
Further sources of information
The longer (old) indicator versions have also been updated
  Aim to make them available in WISE freshwater
Dashboards provide further possibilities for data exploration and quality control
  Aim to publish selected dashboards

## Slide 11
Data – quality control – what we do
Both automatic and manual quality control (QC)
  Flagged records frequently excluded from analyses (depending on the flag)
  Dataset should be as correct but also as extensive as possible
QC issues discovered and summarised per country
  Will get back to you with specific questions as far as time allows
Manual QC mainly focused on the near-complete time series
  If we start to include all sites in the time series analysis, detailed data examination will be difficult
  Your help in improving the data quality is (as always) very valuable

## Slide 12
Data – quality control – how you can help
Reported data are available through discodata or direct download
Please check
  Metadata statements: QC flags with explanation
    Flagged records can be re-submitted as corrected (new values) or confirmed (resultObservationStatus = ‘A’) (Use the 'A' observation status flag to confirm that the given record is correct. The flag should not be applied to all valid records. It is intended for confirmation of extremely high or low values or for other special cases where confirmation is needed or is relevant)
monitoringSiteIdentifier | parameterWaterBodyCategory | observedPropertyDeterminandLabel | resultUom | phenomenonTimeSamplingDate | resultObservedValue | resultObservationStatus | metadata_statements |  |  |  |  | 
 | RW | Phosphate | mg{P}/L | 20141119 | 2.479 |  | QC_OUTLIER_STDEV: Possible outlier - fails in the standard deviation limit test |  |  |  |  | 
Notes:   Discodata: https://discodata.eea.europa.eu/#
  Downloading waterbase: https://www.eea.europa.eu/data-and-maps/data/waterbase-water-quality-icm-2

## Slide 13
Data – quality control – how you can help
Please check
  Site list:
    Changes in site codes over time? Data from the same site are registered to different sites – loss of long time series (e.g. many time series from a country end in 2012 while others start in 2013)
    Some countries have reported a large number of sites with very few years of data in the past – should these sites be part of our new time series analysis?
  Unit errors: Mix-up of NO3-N and NO3 or NH4-N and NH4
    Seen as break-points in time series across all/most sites from a country
    If discovered records will have the flag QC_OUTLIER_EXPERT_YEAR

## Slide 14
Data - LOQ
Observed values not used when reported as below LOQ
  Currently replaced by LOQ value in analyses
  Changes in data dictionary: No need to report observed value when <LOQ
Important that LOQ value is reported and correct
  New QC test on max LOQ in CDR
  Feedback welcome
Older data with unreasonably high LOQ will be flagged and excluded
  Flagged records can be checked and corrected
  Sometimes both the LOQ value and the <LOQ reporting seem wrong (i.e. reported observed value seems reasonable)
observedPropertyDeterminandCode | observedPropertyLabel | resultUom | maxLOQ
CAS_14798-03-9 | Ammonium | mg{NH4}/L | 0.064
EEA_3133-01-5 | BOD5 | mg{O2}/L | 1.2
EEA_3133-02-6 | BOD7 | mg{O2}/L | 1.2
EEA_3164-01-0 | Chlorophyll a | ug/L | 2
EEA_3133-05-9 | Dissolved organic carbon (DOC) | mg{C}/L | 1
CAS_14797-55-8 | Nitrate | mg{NO3}/L | 0.89
CAS_14797-65-0 | Nitrite | mg{NO2}/L | 0.066
CAS_14265-44-2 | Phosphate | mg{P}/L | 0.02
EEA_3133-06-0 | Total organic carbon (TOC) | mg{C}/L | 1
EEA_3161-02-2 | Total oxidised nitrogen | mg{N}/L | 0.2
CAS_7723-14-0 | Total phosphorus | mg{P}/L | 0.03

## Slide 15
Data – fraction
Please report the correct fraction
  Fraction is part of the criteria when we select data to use
  Several examples of impossible reporting
    e.g. BOD5 in spm fraction or total organic carbon in dissolved

## Slide 16
Data – and finally..
Please report disaggregated data when available

## Slide 17
WISE-6 biological data
New biological indicators under development
WISE data used also to study biological responses
  Essential for evaluating responses to measures
How can we study this?
  Linking pressure-state-impact data
  Data sources:
  WISE-6 biology: Chlorophyll a, Cyanobacteria biomass and percentage, Total phytoplankton biomass (and Secchi depth)
  WISE-2 EQR (Ecological Quality ratio) of different biological quality elements
  WFD ecological status of different biological quality elements
  WFD pressures and WISE-1 emissions

## Slide 18
Chlorophyll a time series
Many complete time series available for lakes
More data in the full dataset
  Reporting steadily increasing in some countries
  Dataset dominated by some countries
  Increased reporting would improve representativity
1990
2010
2020
2000
2
10
8
6
4
Chlorophyll a in lakes (µg/l)
156
285

## Slide 19
Impact of eutrophication and CC on human health
  Cyanobacteria are a threat to many ecosystem services and seems to increase with climate change
    Warming – more rapid growth
    Higher frequency of extreme rain events - more nutrient run-off from agricultural land and wastewater overflows
  How are the cyanobacterial blooms developing in Europe?
  Highly relevant topic, but currently too few countries report data to allow a representative picture, and time series are short
  What are the bottlenecks to reporting? Feedback very welcome
Cyanobloom in Norway’s largest lake Mjøsa in 2019, the same happened in 2021
Cyanobacteria:

## Slide 20
Globevnik Lidija, Kari Austnes, 15.10.2021
For reporting!!