2012 Validation questions – Groundwater quality

Dear colleagues,

thank you for participation in 2011 WISE SoE data delivery. During the check of data delivered by member states against logical validation rules, we have found data breaking these rules.

Validation rules are divided into following groups

1) Logical validation rules

2) Data consistency rules

3) Checking of outliers

4) Spatial data checking

5) Monitoring stations checking summary

6) Critical QA issues

Remark: Numbers of rules were updated to follow the numbers used in published European groundwater dataset (http://www.eea.europa.eu/data-and-maps/data/waterbase-groundwater-8)

and in corresponding document Waterbase_Groundwater_v12_QAdocuments.zip

1) Logical validation rules:

Information concerning rules violation is stored on separate sheets for aggregated and disaggregated data.

Aggregated data records are sorted by year, then by determinant and then by groundwater body, disaggregated data records are sorted by year, then by station and then by determinant. This order of sorting, different for aggregated and disaggregated data, comes out from the form in which data are delivered and logically located.

List of rules violated by mentioned data follows at the end of each record (some aggregated data records violate more than one rule).

Aggregated Data:

| Rule | Description |
| --- | --- |
| 201 | Mean >= Minimum |
| 202 | Mean <= Maximum |
| 203 | Median >= Minimum |
| 204 | Median <= Maximum |
| 205 | Minimum <= Maximum |
| 210 | All Values >= 0 tested as (Minimum > 0 AND Mean > 0 AND Maximum > 0 AND Median > 0) Zero value is allowed for Dissolved Oxygen only |
| 211 | IF NumberOfSamples = 1 THEN (Minimum = Mean = Maximum = Median) |
| 213 | IF NumberOfSamples = 0 THEN (AllValueType Is NULL) tested as IF NumberOfSamples = 0 THEN (Minimum = Mean = Maximum = Median = NULL) |
| 241 | If detailed site types fields (Drinking_Water_Sites, Industrial_Sites, Surveillance_Sites, Other_Sites) are provided, then NumberOfSites must be provided as well. |
| 242 | If DeterminandCode-agg = 503 (Dissolved Oxygen), then Class_4 can not be provided (Class_4 have to be equal 0 or NULL in such case). If DeterminandCode-agg = 500 (Nitrate), 501 (Ammonium) or 503 (Dissolved Oxygen), then Class_5 can not be provided (Class_5 have to be equal 0 or NULL in such case). |

According to the groundwater expert evaluation, Mean is the most important value for aggregated data from the point of view of data efficiency. On this account, all aggregated data records containing at least Mean value > 0 and passing rules 201 – 205 were accepted  (for example combinations: “Mean > 0, Minimum = Maximum = Median = NULL” or “Mean > 0, Median > 0, Minimum = Maximum = NULL”).

In case any of the reported agregated values (Minimum, Mean, Maximum or Median) is (are) marked as wrong for certain data record and you will correct it (them), please check remaining of these four aggregated values and Classification classes (fields Class_1 …Class_5) as well, mark them as correct, correct them or set them as NULL.

Disaggregated Data:

| Rule | Description |
| --- | --- |
| 210 | All Values > 0 (excluding Dissolved Oxygen and Hydrogen Carbonate (Bicarbonate, HCO3)) |

According to the Data Dictionary requests, the values “below the limit of detection (LOD)” (reported value in brackets: e.g. “[0.01]”) or “below the limit of quantification (LOQ)” (reported value has prefix „<“ – e.g. „<0.01”) have to be used instead of zero value in the case rule 210 is violated. Both limits are always > 0. In such case, one half of the limit value is used for data aggregation by ETC.

In the case you are not able provide us the proper LOD or LOQ values for records violating rule 210 (e.g. in the case of older data), please inform us, whether we can to remove these “zero” records from the database

2) Data consistency rules

Aggregated data:

- Aggregated data record must contain data at least in the following fields:

groundwater body ID,

year,

mean

- Groundwater body country code must be stored in the database

- Groundwater body ID must be stored in the database

- Determinand code – agg must be stored in the database

Disaggregated data:

- Disaggregated data record must contain data in all four fields:

monitoring station ID,

determinand code,

value,

date (year at least)

- Monitoring station ID must be stored in the database and must be related to the groundwater body ID, which is stored in the database

- Determinand code must be stored in the database

(exception: reporting of substances not mentioned in the codelist; in such case the substance CAS Number and / or Name should  be provided in Determinand code field)

Monitoring stations:

- Monitoring station country code (first 2 characters of station ID) must be stored in the database

- Monitoring station must be linked to the groundwater body ID, which is stored in the database

Groundwater bodies:

- Groundwater body country code (first 2 characters of gw body ID) must be stored in the database

Saltwater intrusion areas:

- Saltwater intrusion area country code (first 2 characters of Saltwater intrusion area ID) must be stored in the database

- Saltwater intrusion area must be linked to the groundwater body ID, which is stored in the database

3) Checking of outliers

All outlier rules are violated only if given value has not been confirmed by country as correct.

Simple outliers

Checking of delivered concentration value (aggregated or disaggregated) against potentially low / high values to detect unit errors, decimal order errors, typing errors, etc.

Aggregated data

| Rule | Description |
| --- | --- |
| 417 | Potentially low values: NO3, NH4, NO2 < 0.0001 mg/l |
| 418 | Potentially high values: NO3 Nitrate 1000 mg/l NH4 Total Ammonium 1000 mg/l NO2 Nitrite 100 mg/l O2 Dissolved Oxygen 1000 mg/l |

Disaggregated data

| Rule | Description |
| --- | --- |
| 417 | Potentially low values: NO3, NH4, NO2 < 0.0001 mg/l Preferred SoE hazardous substances: < 0.0001 µg/l |
| 418 | Maximum values: Temperature (water) 100°C pH 14 Potentially high values: Nutrients: NO3 Nitrate 1000 mg/l NH4 Total Ammonium 1000 mg/l NO2 Nitrite 100 mg/l O2 Dissolved Oxygen 1000 mg/l Total dissolved solids 2500 mg/l Preferred SoE Hazardous substances: metals: 10000 µg/l other substances: 10 µg/l (see details in Appendix 1. below) |

Complex outliers

Outliers checking rules are specified according to the expert’s judgement by following way:

Aggregated data:

values out of the range of +- 3x standard deviation from an average of the whole time serie are considered as potential outliers

| Rule | Description |
| --- | --- |
| 411 | value deviation > +/-3σ from the mean value calculated for aggregated data per determinand, groundwater body and whole time span |

Disaggregated data:.

- values out of the range of ± 3 x standard deviation from an average of the time serie within one year are considered as potential outliers

- values out of the range of ± 5.5 x standard deviation  from an average of the time serie within whole reported period are considered as potential outliers

| Rule | Description |
| --- | --- |
| 413 | value deviation > ± 3σ from the mean value calculated for disaggregated data per determinand, station and year |
| 414 | value deviation > ± 5.5σ from the mean value calculated for disaggregated data per determinand, station and whole time span |

Outlier detection method was determined by senior groundwater expert based on long-term experience. Please check and evaluate the values marked as outliers. In the case the initially reported outliers are not correct, send us the repaired values, if possible. Reporting the corrected value (or information correct / not correct at least) in the next free column of the .xls table in which outliers are reported will be preferred. Your remarks to correct values which were marked as outliers are very appreciated as well.

4) Spatial data checking

Delivered polygons of groundwater bodies and coordinates of groundwater monitoring stations are checked by data manager using GIS software according to the boundaries of the relevant country. Euro Regional Map country boundaries are used for this checking.

5) Monitoring stations checking summary

| Rule | Description |
| --- | --- |
| 501 | station coordinates fall outside the respective country boundary |
| 502 | one or both station coordinates are missing |
| 503 | more stations with identical coordinates (if it might indicate an error of coordinates) |
| 531 | station can not be linked to any of the groundwater body provided in the respective table (link to groundwater body is missing) |

6) Critical QA issues

Reply to critical QA issues on previously reported data is one of criteria requested for the best scoring (3 positive smileys).

Following Critical QA issues were specified for groundwater reporting:

a) missing coordinates of active monitoring stations (if not secret for security reasons – e.g. selected drinking water sources)

b) missing link from active monitoring station to WFD groundwater body (EU countries only)

c) missing RBDcode attribute for WFD gw bodies (EU countries only)

active monitoring station = currently used

======================================================================

Reporting the corrected value in the next free columns of the .xls table in which wrong values are reported will be preferred (Please do not forget to give the proper name to the newly added fields – eg. corr_mean, corr_max,…). Another possibility is to copy the file with list of wrong values and substitute the wrong values by corrected ones. In such case, add the string “corr” or “corrected” to the name of this file.

We would like to ask you for data correction and re-delivery if possible. We are enclosing a spreadsheet with erroneous data. Please submit corrected data via CDR (preferably) or you can use e-mail address below for further contact and clarification.

Thank you for your understanding and cooperation.

Miroslav Fanta

ETC / ICM Data Manager, groundwater working database manager

CENIA

e-mail: miroslav.fanta@cenia.cz

1st of August 2012

Appendix 1:

Groundwater: Preferred SoE Hazardous Substances and Potentially high values

| CAS | Name | DeterminandCode | Unit | Preferred SoE Haz.Subst. | Potentially high values |
| --- | --- | --- | --- | --- | --- |
| 15972-60-8 | Alachlor | 504 | µg/l | Yes | 10 |
| 1912-24-9 | Atrazine | 505 | µg/l | Yes | 10 |
| 470-90-6 | Chlorfenvinphos | 506 | µg/l | Yes | 10 |
| 2921-88-2 | Chlorpyrifos | 507 | µg/l | Yes | 10 |
| 330-54-1 | Diuron | 508 | µg/l | Yes | 10 |
| 58-89-9 | Gamma-HCH (Lindane) | 510 | µg/l | Yes | 10 |
| 118-74-1 | Hexachlorobenzene (HCB) | 511 | µg/l | Yes | 10 |
| 34123-59-6 | Isoproturon | 512 | µg/l | Yes | 10 |
| 122-34-9 | Simazine | 513 | µg/l | Yes | 10 |
| 1582-09-8 | Trifluralin | 514 | µg/l | Yes | 10 |
| 7440-38-2 | Arsenic | 803 | µg/l | Yes |  |
| 7440-50-8 | Copper | 804 | µg/l | Yes | 10000 |
| 7440-66-6 | Zinc | 807 | µg/l | Yes | 10000 |
| 7440-43-9 | Cadmium | 808 | µg/l | Yes | 10000 |
| 7440-47-3 | Chromium | 813 | µg/l | Yes |  |
| 7440-02-0 | Nickel | 815 | µg/l | Yes | 10000 |
| 7439-92-1 | Lead | 819 | µg/l | Yes | 10000 |
| 7439-97-6 | Mercury | 822 | µg/l | Yes |  |
| 87-86-5 | Pentachlorophenol | 823 | µg/l | Yes |  |
| 309-00-2 | Aldrin | 825 | µg/l | Yes | 10 |
| 789-02-6 | DDT, o,p' | 827 | µg/l | Yes | 10 |
| 50-29-3 | DDT, p,p' | 828 | µg/l | Yes | 10 |
| 72-55-9 | DDE, p,p' | 831 | µg/l | Yes | 10 |
| 72-54-8 | DDD, p,p' | 834 | µg/l | Yes | 10 |
| 60-57-1 | Dieldrin | 835 | µg/l | Yes | 10 |
| 72-20-8 | Endrin | 836 | µg/l | Yes | 10 |
| 25057-89-0 | Bentazone | 839 | µg/l | Yes | 10 |
| 319-84-6 | Alpha-HCH | 840 | µg/l | Yes | 10 |
| 319-85-7 | Beta-HCH | 841 | µg/l | Yes | 10 |
| 959-98-8 | Alpha-Endosulfan | 845 | µg/l | Yes | 10 |
| 6190-65-4 | Desethylatrazine | 849 | µg/l | Yes | 10 |
| 1007-28-9 | Desisopropylatrazine | 850 | µg/l | Yes | 10 |
| 139-40-2 | Propazine | 851 | µg/l | Yes | 10 |
| 7287-19-6 | Prometryn | 852 | µg/l | Yes | 10 |
| 5915-41-3 | Terbuthylazine | 854 | µg/l | Yes | 10 |
| 886-50-0 | Terbutryn | 855 | µg/l | Yes | 10 |
| 94-75-7 | 2,4-D | 861 | µg/l | Yes | 10 |
| 94-74-6 | MCPA | 864 | µg/l | Yes | 10 |
| 7085-19-0 | Mecoprop | 866 | µg/l | Yes | 10 |
| 120-12-7 | Anthracene | 877 | µg/l | Yes | 10 |
| 71-43-2 | Benzene | 878 | µg/l | Yes |  |
| 85535-84-8 | Chloroalkanes C10-13 | 883 | µg/l | Yes |  |
| 107-06-2 | 1,2-Dichloroethane | 884 | µg/l | Yes |  |
| 75-09-2 | Dichloromethane | 885 | µg/l | Yes |  |
| 117-81-7 | Di (2-ethylhexyl) phthalate (DEHP) | 886 | µg/l | Yes |  |
| 87-68-3 | Hexachlorobutadiene (HCBD) | 891 | µg/l | Yes |  |
| 91-20-3 | Naphthalene | 892 | µg/l | Yes |  |
| 104-40-5 | 4-nonylphenol | 894 | µg/l | Yes |  |
| 140-66-9 | Para-tert-octylphenol | 897 | µg/l | Yes |  |
| 608-93-5 | Pentachlorobenzene | 898 | µg/l | Yes |  |
| 50-32-8 | Benzo(a)pyrene | 900 | µg/l | Yes | 10 |
| 205-99-2 | Benzo(b)fluoranthene | 901 | µg/l | Yes | 10 |
| 191-24-2 | Benzo(g,h,i)perylene | 902 | µg/l | Yes | 10 |
| 207-08-9 | Benzo(k)fluoranthene | 903 | µg/l | Yes | 10 |
| 206-44-0 | Fluoranthene | 904 | µg/l | Yes | 10 |
| 193-39-5 | Indeno(1,2,3-cd)pyrene | 905 | µg/l | Yes | 10 |
| 67-66-3 | Trichloromethane | 912 | µg/l | Yes |  |
| 465-73-6 | Isodrin | 916 | µg/l | Yes | 10 |
| 330-55-2 | Linuron | 917 | µg/l | Yes | 10 |
| 79-01-6 | 1,1,2-trichloroethene | 1111 | µg/l | Yes |  |
| 127-18-4 | 1,1,2,2-tetrachloroethene | 1112 | µg/l | Yes |  |
| 56-23-5 | Tetrachloromethane | 1113 | µg/l | Yes |  |
| 71-55-6 | 1,1,1-trichloroethane | 1246 | µg/l | Yes |  |
| 7440-50-8 | Copper dissolved | 1291 | µg/l | Yes | 10000 |
| 7440-66-6 | Zinc dissolved | 1292 | µg/l | Yes | 10000 |
| 7440-43-9 | Cadmium dissolved | 1293 | µg/l | Yes | 10000 |
| 7440-02-0 | Nickel dissolved | 1294 | µg/l | Yes | 10000 |
| 7439-92-1 | Lead dissolved | 1295 | µg/l | Yes | 10000 |
| 7440-38-2 | Arsenic dissolved | 1315 | µg/l | Yes |  |
| 7439-97-6 | Mercury dissolved | 1317 | µg/l | Yes |  |
| 7440-47-3 | Chromium dissolved | 1318 | µg/l | Yes |  |