Logical rule violation tests

The Violation checks were performed on data according to basic validation rules. The following table explains and contains the matching between the rules applied and the numbers we found in the column QA_LRviolations:

| Rule | Basic validation rules |
| --- | --- |
| 1 | Mean >= Minimum |
| 2 | Mean <= Maximum |
| 3 | Median >= Minimum |
| 4 | Median <= Maximum |
| 5 | Minimum <= Maximum |
| 6 | StandardDeviation < Maximum |
| Rule | Combined validation rules |
| 13 | IF Minimum < Maximum THEN (StandardDeviation > 0) |
| 14 | IF NumberOfSamples = 1 THEN (Mean = Minimum = Maximum = Median) |
| 15 | IF NumberOfSamples = 1 THEN (StandardDeviation = 0) |
| 16 | IF NumberOfSamples = 0 THEN (AllValueType Is Null) |
| Rule | Negative value validation rule |
| 17 | All Values |

Potential outliers

These DATA seem to divert from “normal” values.

Two statistical tests used:

- Q-Test

- Z-Test

Also chemical rules applied:

- BOD5 < COD,	BOD5 value should always be lower than COD value

- BOD5 < Total Organic Carbon, 	BOD5 value should always be lower than Total Organic Carbon value

- IF BOD5 is high THEN Dissolved Oxygen is low,	If BOD5 value is high (more than 25 µg/l), then Dissolved Oxygen value should be low (less than 4 mg/l O2) and vice versa.

- IF Dissolved Oxygen is high THEN Total Ammonium is low, 	If Dissolved Oxygen values is high (more than 20 mg/l O2), then Total Ammonium value should be low (less than 3 mg/l N)

- IF ph is low (<3) or high (>10) THEN BOD5 cannot be high

- Total Nitrogen = Kjeldahl Nitrogen + Nitrate + Nitrite

- Kjeldahl Nitrogen = Organic Nitrogen + Total Ammonium

- Total Oxidised Nitrogen = Nitrate + Nitrite

- Total Phosphorus > Orthophosphate

A list of time series for each outlier which shows all year values for this station/determinant. Outlier is marked with red and flagged with field QA_outlier = 1.

QA_outlier field values:

Existing values:

0 - value is not an outlier

1 - value is suspected to be an outlier

The column (Explanation) must be filled by countries if data we request is not erroneous.