| EEA/ADS/06/001 – Water |  |
| --- | --- |

Validation questions to member countries

List of Rules and Checks Applied in Lakes’ Database

Version: 0.1

Date: 15/7/2009

EEA Task: 1.5.1.2 A) WISE SoE data capture

ETC/Water Activity Number : 7

Prepared by / compiled by: George Papoutsoglou

Organisation : NTUA

EEA Project manager: Marek Staron/Hermann Peifer

Version History

| Version | Date | Author | Status and description | Distribution |
| --- | --- | --- | --- | --- |
| 0.1 | 15/07/2009 | George Papoutsoglou | Final version for EEA | CIRCA / Miroslav Fanta |

Contents

A. TABLE: lakes_v9_quality (Nutrients)	3

1. Logical rules for data validation:	3

2. Outliers Checks:	4

3. Chemical violation rules applied:	4

B. TABLE: lakes_v9_hazsub (Hazardous Substances)	5

1. Outliers Checks:	5

C. TABLE: lakes_v9_stations (Stations’ Characteristics)	7

### Lakes Database

## A. TABLE: lakes_v9_quality (Nutrients)

| Field | Rule |
| --- | --- |
| CountryCode NationalStationID Year AggregationPeriod Determinand_Nutrients | - These are key fields: must have a unique value (no duplicates allowed) and must not be left blank |
| Mean * Minimum * Maximum * Median * StandardDeviation * NumberOfSamples NoOfSubsites SampleDepth Alkalinity Conductivity pH | - Float data type: fields must contain only decimals, if there are any other characters in these fields, must be reported separately, e.g. <, > - Values have to be greater or equal 0 * for determinand “Temperature” values can be also be below 0 |
| Determinand_Nutrients | - Determinands have to be from the standard subset which can be found here: http://dd.eionet.europa.eu/data_element.jsp?mode=view&delem_id=36622 |
| Unit_Nutrients | - each determinand has its own unit, appropriate units for each determinand can be found here: http://dd.eionet.europa.eu/data_element.jsp?mode=view&delem_id=31969 |

### 1. Logical rules for data validation:

The Violation checks were performed on data according to basic validation rules. The following table explains and contains the matching between the rules applied and the numbers we found in the column QA_LRviolations:

| Validation Rule Number | Basic Validation Rule |
| --- | --- |
| 1 | Mean >= Minimum |
| 2 | Mean <= Maximum |
| 3 | Median >= Minimum |
| 4 | Median <= Maximum |
| 5 | Minimum <= Maximum |
| 6 | StandardDeviation < Maximum |

| Validation Rule Number | Combined Validation Rule |
| --- | --- |
| 13 | IF Minimum < Maximum THEN (StandardDeviation > 0) |
| 14 | IF NumberOfSamples = 1 THEN (Mean = Minimum = Maximum = Median) |
| 15 | IF NumberOfSamples = 1 THEN (StandardDeviation = 0) |
| 16 | IF NumberOfSamples = 0 THEN (AllValueType Is Null) |

| Validation Rule Number | Negative Value Validation Rule |
| --- | --- |
| 17 | All Values > 0 |

### 2. Outliers Checks:

The Outliers checks were performed on data according to statistical methods (Q-Test, Z-Test etc.), in order to detect erroneous values for each determinand for the lakes quality data. The following table explains and contains the matching between the rules applied and the numbers we found in the column QA_Outlier:

| Value | Outlier Type Definition |
| --- | --- |
| 1 | standard potential outlier - value is either higher/lower than limit value or is suspiciously high/low comparing to the rest of the time series or value change between two consecutive values is suspiciously abrupt or is marked as an outlier by a content expert |
| 2 | measurements are probably taken from a highly polluted locations |
| 3 | the whole country delivery is considered as problematic because it contains too many quality issues |
| 10 | Tested value (Mean) = 0 |
| 99 | Tested value (Mean) Is Null |

### 3. Chemical violation rules applied:

The Chemical Violation checks were performed on data according to basic validation rules. The following table explains and contains the matching between the rules applied and the numbers we found in the column QA_CRviolations:

| Value | Rule Violated |
| --- | --- |
| 1 | BOD5 < COD |
| 2 | BOD5 < TotalOrganicCarbon |
| 3 | Orthophosphate < TotalPhosphorus |
| 4 | Total Nitrogen = Kjeldahl Nitrogen + Nitrate + Nitrite (+-5% toleration if all values available) |
| 5 | Kjeldahl Nitrogen = Organic Nitrogen + Total Ammonium (+-5% toleration if all values available) |
| 6 | Total Oxidised Nitrogen = Nitrate + Nitrite (+-5% toleration if all values available) |

## B. TABLE: lakes_v9_hazsub (Hazardous Substances)

| Field | Rule |
| --- | --- |
| CountryCode NationalStationID Year * Month * Day * Determinand_HazSubs | - These are key fields: must have a unique value (no duplicates allowed) and must not be left blank * Year must not be greater than current year * Month must be in 1-12 range * Day must be in 1-31 range |
| NoOfSubsites NumberOfSamples Hardness SuspendedParticulateMatter DissolvedOrganicMatter pH Ca Mg Na K HCO3 Cl SO4 | - Float data type: fields must contain only decimals, if there are any other characters in these fields, must be reported separately, e.g. <, > - Values have to be greater or equal 0 |

### 1. Outliers Checks:

If data values are greater than “Potentially High Average Value” there could be an error:

| Standard Determinand Name | Standard Unit | Potentially High Average Value |
| --- | --- | --- |
| Methoxychlor | ug/l | 0,03 |
| Endrin | ug/l | 0,036 |
| MALATHION | ug/l | 0,1 |
| DIAZINON | ug/l | 0,17 |
| Dieldrin | ug/l | 0,056 |
| Heptachlor | ug/l | 0,0038 |
| Lindane (gamma-HCH) | ug/l | 0,95 |
| alpha-Endosulfan | ug/l | 0.056 |
| Mercury and its compounds | ug/l | 0,77 |
| Zinc and its compounds | ug/l | 120 |
| Copper and its compounds | ug/l | 9 |
| Pentachlorophenol | ug/l | 15 |
| Cadmium and its compounds | ug/l | 0,25 |
| CYANIDE - AS CN | ug/l | 5,2 |
| Aldrin | ug/l | 3 |
| Arsenic and its compounds | ug/l | 150 |
| Nickel and its compounds | ug/l | 52 |
| Chromium and its compounds | ug/l | 74 |
| Lead and its compounds | ug/l | 2,5 |
| Iron and its compounds | ug/l | 1000 |
| Polychlorinated biphenyls | ug/l | 0,014 |

The Outliers checks were performed on data according to potentially high average values rules. The following table explains and contains the matching between the rules applied and the numbers we found in the column QA_Outlier:

| Value | Outlier Type Definition |
| --- | --- |
| 1 | standard potential outlier - value is either higher/lower than limit value or is suspiciously high/low comparing to the rest of the time series or value change between two consecutive values is suspiciously abrupt or is marked as an outlier by a content expert |
| 2 | measurements are probably taken from a highly polluted locations |
| 3 | the whole country delivery is considered as problematic because it contains too many quality issues |
| 10 | Tested value (Mean) = 0 |
| 99 | Tested value (Mean) Is Null |

## C. TABLE: lakes_v9_stations (Stations’ Characteristics)

| Field | Rule |
| --- | --- |
| CountryCode NationalStationID | - These are key fields: must have a unique value (no duplicates allowed) and must not be left blank |
| Longitude Latitude | - Stations coordinates must not be left blank - must be within European boundaries |

Spatial and Logical checks were performed on data according to the geographical position of the stations reported as well as the physical characteristics of each station and the corresponding lake they belong. The following table explains and contains the matching between the rules applied and the numbers we found in the column QA_station_problem:

| Value | Problem or Error Description |
| --- | --- |
| 1 | station coordinates fall outside the respective country boundary |
| 2 | station coordinates are missing |
| 3 | coordinates fall outside the respective river basin district |
| 4 | more stations with the same coordinates |
| 11 | altitude is suspicious or illogical |
| 12 | catchment area is suspicious or illogical |
| 13 | lake area is suspicious or illogical |
| 14 | lake depth is suspicious or illogical |
| 99 | station is not defined in the stations table |