- Automatic QA errors

In your delivery on 24.9.2009, automatic QA has found the following errors for the two files: 
Basicquality: 
- some duplicates 
- some data values are negative 
- some determinands have non-standard units 
- some records do not comply to logical rules, i.e. Minimum > Maximum 
Details about the errors: 
http://cdr.eionet.europa.eu/hu/eea/ewn1/envstw0yg/AutomaticQA_47514_1253819766 
(link is password-protected and can be accessed by data provider in CDR)

Impactquality: 
- some records have value 18 for Month, Month should be from 1-12 interval 
Details about the errors: 
http://cdr.eionet.europa.eu/hu/eea/ewn1/envstw0yg/AutomaticQA_47511_1253822890 
(please ignore a long list of errors on "3. Duplicates", only "4. Data Types" is relevant) 
For EEA indicators CSI019 and CSI022, violations of logical and chemical rules and outliers are excluded.

- zero data values

Some determinands in table “Basicquality” have zero values (min, mean, max, standard deviation) (2777 records with zero values). Some determinands in table “ImpactQuality” have zero values under “concentration” field (27015 records with zero values). Are zero values under the limit of detection or limit of determination?

- high Orthophosphate values

After thorough examination of your data we found that most Orthophosphate values reported for 2007 are obviously wrong (too high). Overalll average for 1992-2006 is 0.28 mg/l P; average for 2007 is 169 mg/l P. All values reported for 2007 have Mean value either >10 (wrong) or <1 (presumeably right). 

Most likely, the wrong values have unit µg/l P instead of mg/l P. Can you confirm that or is there any other problem with the data?