| EEA/NSV/10/002 – ETC/ICM |  |
| --- | --- |

Validation questions to
Member Countries

Version: 1.0

Date: 29/7/2011

ETC/ICM task: 1.4.1.a-1 WISE SoE priority data flows

Milestone: 2 – Validation Questions for Member States

Prepared by / compiled by: George Karavokiros

Organisation: NTUA

EEA project manager: Marek Staron

Version history

| Version | Date | Author | Status and description | Distribution |
| --- | --- | --- | --- | --- |
| 1.0 | 29/07/2011 | George Karavokiros | Final version | CIRCA, MST, AKU, MFA |

Contents

Letter to the NFPs	2

1	Rules embedded in the WQ Reporting Tool	2

1.1	Basic rules (not unique ID, mandatory field empty, false data type etc.)	2

1.2	Logical rules	2

1.3	Outliers and range checks	2

1.4	Areal rules (regional water balance, regional water abstraction, regional water use)	2

1.4.1	Introduction	2

1.4.2	Rule definitions	2

2	Outlier rules in hydrological time series	2

2.1	Extreme value checks	2

2.2	Temporal consistency checks	2

# Letter to the NFPs

July 2011

Dear Colleagues,

As you know this was the second time WQ was included as a WISE-SoE data flow. In the last two years WQ data from 23 countries have been reported (see. wq-dreams.eu). This is a positive development which could be achieved only with your active help.

For the next years we aim to increase the density of water quantity data reducing further data gaps in Europe, especially for parameters which are crucial for the assessment of water scarcity and droughts and the vulnerability of water resources in Europe. In this process quality assurance of the reported data is an important step and our goal is to constantly enhancing the validity of the data in cooperation with you.

Coming to this year’s validation questions, as you know the WQ Reporting Tool ensures that the data you are reporting are error-free from certain error types (e.g. data type, duplicate stations, range errors, mandatory fields etc.). The rules embedded in the tool, along with analytical explanations, are listed in chapter 1.

Although the Tool prevents certain types of errors, this does not necessarily mean that the provided data were completely error free. Especially validation checks for outliers cannot be made at the source, requiring further information (e.g. country border lines for checking the stations correct placement, long time series, etc.). Having run these checks for the whole dataset we may have encountered some issues, listed in your county’s folder in the CDR, which you are kindly asked to help us resolve. You may also notice that some questions refer to past reportings as well, since some validation routines have been applied this year for the first time.

When reading the validation questions and especially those referring to outliers, keep in mind that the list of outliers has been generated automatically from the WISE-SoE#3 Water Quantity database and is based on a number of generic outlier rules which apply to most hydrometeorological timeseries. These routines check the database for extreme values and verify the temporal consistency of time series (see chapter 2). For the parameterization of the rules the variable type and the time step of the time series have been taken into account. The identified outliers may be caused by errors in the measuring or the reporting procedure. This does not necessarily mean that the listed cases are actually errors. In most of these cases they are probably just extreme phenomena or special cases, an assumption we would like you to confirm. If you think that a listed outlier is not an error please let us know (with your next reporting or directly by sending an email to me), so that you will not be asked again for this validation next year. Otherwise, please send along with your next reporting a new corrected data file containing the corrected data.

Thank you once again for your cooperation

George Karavokiros

# Rules embedded in the WQ Reporting Tool

The following rules are embedded in version 1.2 of the Water Quantity Reporting Tool.

## Basic rules (not unique ID, mandatory field empty, false data type etc.)

| Code | Definition | Rule viol. type | Remarks |
| --- | --- | --- | --- |
| BA001 | A real number is expected for the field: XXX | error | This rule applies to a number of variables in various forms e.g. the groundwater level |
| BA002 | A positive real number is expected for the field: XXX | error | This rule applies to a number of variables in various forms e.g. the reservoir storage capacity |
| BA003 | A positive real number or zero is expected for the field/grid: XXX | error | This rule applies to a number of variables in various forms e.g. inflow/outflow volume, streamflow |
| BA004 | A positive integer number is expected for the field: XXX | error | This rule applies to a number of variables in various forms e.g. year, SRID |
| BA005 | The person responsible for the data entry should be specified | error | You may enter the correct information from the main form |
| BA006 | The email address of the person responsible for the data entry should be specified | error | You may enter the correct information from the main form |
| BA007 | A country has to be selected first | error | You may select the country from the main form |
| BA008 | A unique identifier for the station/reservoir is missing | error | This rule applies to rain gauge stations, reservoirs, stream flow stations and wells |
| BA009 | A station/reservoir with ID XXX already exists | error | This rule applies to rain gauge stations, reservoirs, stream flow stations and wells |
| BA010 | A coordinate system has to be defined | error | This rule applies to rain gauge stations, reservoirs, stream flow stations and wells |
| BA011 | A projection system should been defined | warning | This rule applies to rain gauge stations, reservoirs, stream flow stations and wells |
| BA012 | This station is neither a EIONET nor a WFD station | warning | This rule applies to rain gauge and stream flow stations |
| BA013 | No data have been entered. You may want to check the data tab | warning | This rule applies to reservoirs, stream flow stations and wells |
| BA014 | The type of the reservoir must be selected | error | This rule applies to reservoirs |
| BA015 | Column “Item class” in table XXX may have only values between 1 and 3 | error | This rule applies only to the 2nd column of the tables in the tab “Large items” in the form Water use |

## Logical rules

| Code | Definition | Rule viol. type | Remarks |
| --- | --- | --- | --- |
| LO001 | The monthly values in table: XXX and column: XXX do not sum up to the annual value | error | This rule applies to all variables if annual and monthly data is given |
| LO002 | Min. streamflow value should be lower or equal than Max. streamflow value | error | This rule applies to stream flow stations |

## Outliers and range checks

| Code | Definition | Rule viol. type | Remarks |
| --- | --- | --- | --- |
| OU001 | A real number between -100 and 5000 is expected for Altitude | error | This rule applies to rain gauge stations, reservoirs, stream flow stations and wells |
| OU002 | An integer number between 1900 and XXX is expected for the LTAA starting year | error | This rule applies to all data related to Long Term Annual Average (LTAA) i.e. station data and regional data. The reference period must lie between 1900 and the reporting year. |
| OU003 | An integer number between 1900 and XXX is expected for the LTAA ending year | error | This rule applies to all data related to Long Term Annual Average (LTAA) i.e. station data and regional data. The reference period must lie between 1900 and the reporting year. |
| OU004 | The reported length period is too small to be representative for LTAA values. The LTAA reference period must be at least 10 years, preferably more than 20 years long | error | This rule applies to all data related to Long Term Annual Average (LTAA) i.e. station data and regional data |
| OU005 | The reported LTAA reference period should be at least 20 consecutive years long | warning | This rule applies to all data related to Long Term Annual Average (LTAA) i.e. station data and regional data |
| OU006 | Value for Longitude not typical for Europe | warning | The value for Longitude appears to be outside the valid range for Europe |
| OU007 | Value for Latitude not typical for Europe | warning | The value for Latitude appears to be outside the valid range for Europe |

## Areal rules (regional water balance, regional water abstraction, regional water use)

### Introduction

The following logical rule definitions consist of two expressions and a relation sign. Both expressions are additions. An equation rule check is passed if one of the following conditions is met:

all variables of the two expressions have valid real values and the two expressions are equal

one expression has variables with invalid values. The rule is checked as an inequality, excluding the invalid value.

both expressions have at least one invalid variable (meaning: unable to check)

An inequality rule check is passed if one of the following conditions is met:

all variables of the greater expression have valid real values and the inequality is true.

at least one variable of the greater expression is invalid (meaning: unable to check)

All rules apply to all temporal scales, i.e. months, seasons and years. Small differences up to 0.1 between the two expressions in equations that may arise due to roundings are tolerated

### Rule definitions

| Code | Definition | Rule viol. type | Remarks / Explanation |
| --- | --- | --- | --- |
|  | Regional Water Balance |  |  |
| WB001 | wb_areal_precipitation = wb_internal_flow + wb_act_evapotranspiration (Equivalent to wb_internal_flow = wb_areal_precipitation - wb_act_evapotranspiration) | error | Areal precipitation must equal the sum of Internal flow plus Actual Evapotranspiration. Negative value for Internal flow is acceptable for a given time step (e.g. summer months). |
| WB002 | wb_pot_evapotranspiration > wb_act_evapotranspiration | error | Potential Evapotranspiration must be more than Actual Evapotranspiration. |
| WB003 | wb_total_actual_outflow_neighbour + wb_total_actual_outflow_sea = wb_total_actual_outflow | error | Total actual outflow must equal the sum of the Total actual outflow into neighbouring areas and the Total actual outflow into the sea. |
| WB004 | wb_returned_before_use + wb_returned_after_use = wb_return_flow | error | Return flow must equal the returned flow before use and the returned flow after use. |
| WB005 | wb_treated_effluent + wb_non_treated_effluent = wb_returned_after_use | error | Returned flow after use must equal the sum of the treated effluent and the non-treated effluent. |
| WB006 | wb_treated_effluent_uwwtp + wb_treated_effluent_other_wwtp = wb_treated_effluent | error | Treated effluent must equal the sum of the treated effluent from UWWTP and the treated effluent from other WWTP. |
| WB007 | wb_non_treated_effluent > wb_non_treated_effluent_cooling + wb_non_treated_effluent_hydropower | error | Non Treated Effluent must be more than the sum of the Non treated effluent from cooling and Non treated effluent from hydropower. |
| WB008 | wb_losses_betwn_use_and_reuse <= wu_total_freshwater_used_total | warning | Losses between use and reuse need to be less than the Total freshwater used. This rule is checked when closing the Water Balance form or the Water Use form |
| WB009 | wb_desalinated_water_domestic + wb_desalinated_water_nace_a + wb_desalinated_water_nace_b + wb_desalinated_water_nace_c + wb_desalinated_water_nace_d + wb_desalinated_water_nace_i + wb_desalinated_water_other = wb_desalinated_water_total | error | Total Desalinated water must equal to the sum of the sectoral desalinated water. |
| WB010 | wb_reused_water_nace_a >= wb_reused_water_nace_a_irrgation | error | Reused water for NACE A must be more than Reused water for NACE A irrigation. |
| WB011 | wb_reused_water_nace_c >= wb_reused_water_nace_c_cooling | error | Reused water for NACE C must be more than Reused water for NACE C cooling. |
| WB012 | wb_reused_water_nace_d >= wb_reused_water_nace_d_cooling | error | Reused water for NACE D must be more than Reused water for NACE D cooling. |
| WB013 | wb_reused_water_domestic + wb_reused_water_nace_a + wb_reused_water_nace_b + wb_reused_water_nace_c + wb_reused_water_nace_d + wb_reused_water_nace_i + wb_reused_water_other = wb_reused_water_total | error | Total Reused water must equal to the sum of the sectoral reused water. |
| WB014 | wb_desalinated_water_nace_a >= wb_desalinated_water_nace_a_irrgation | error | Desalinated water for NACE A must be more than Desalinated water for NACE A irrigation. |
| WB015 | wb_desalinated_water_nace_c >= wb_desalinated_water_nace_c_cooling | error | Desalinated water for NACE C must be more than Desalinated water for NACE C cooling. |
| WB016 | wb_desalinated_water_nace_d >= wb_desalinated _water_nace_d_cooling | error | Desalinated water for NACE D must be more than Desalinated water for NACE D cooling. |
|  | Regional Water Abstraction |  |  |
| WA001 | wa_for_public_wss_sw + wa_abstraction_for_self_suply_total_sw = wa_total_abstraction_sw | error | Will be checked after the submission of the data. Not implemented in the WQ reporting tool. |
| WA002 | wa_for_public_wss_gw + wa_abstraction_for_self_suply_total_gw = wa_total_abstraction_gw | error | Will be checked after the submission of the data. Not implemented in the WQ reporting tool. |
| WA003 | wa_total_abstraction_sw + wa_total_abstraction_gw = wa_total_abstraction | error | Total freshwater abstraction must equal to the sum of the Total freshwater abstraction from surface water and the Total freshwater abstraction from groundwater. |
| WA004 | wa_for_public_wss_sw + wa_for_public_wss_gw = wa_for_public_wss | error | Total freshwater abstraction for public water supply systems must equal to the sum of the Total freshwater abstraction from surface water for public water supply systems and the Total freshwater abstraction from groundwater for public water supply systems. |
| WA005 | wa_total_abstraction_sw >= wa_total_abstraction_for_hydropower | error | Total freshwater abstraction from surface water must be more than the Total freshwater abstraction for Hydropower. |
| WA006 | wa_non_freshwater_domestic + wa_non_freshwater_nace_a + wa_non_freshwater_nace_b + wa_non_freshwater_nace_c + wa_non_freshwater_nace_d + wa_non_freshwater_nace_i + wa_non_freshwater_other = wa_non_freshwater_total | error | Total Abstracted non-freshwater must equal to the sum of the sectoral abstracted non-freshwater. |
| WA007 | wa_non_freshwater_nace_a >= wa_non_freshwater_nace_a_irrgation | error | Abstracted non-freshwater for NACE A must be more than Abstracted non-freshwater for NACE A irrigation. |
| WA008 | wa_non_freshwater_nace_c >= wa_non_freshwater_nace_c_cooling | error | Abstracted non-freshwater for NACE C must be more than Abstracted non-freshwater for NACE C cooling. |
| WA009 | wa_non_freshwater_nace_d >= wa_non_freshwater_nace_d_cooling | error | Abstracted non-freshwater for NACE D must be more than Abstracted non-freshwater for NACE D cooling. |
| WA010 | wa_abstraction_for_self_suply_total_sw_domestic + wa_abstraction_for_self_suply_total_sw_nace_a + wa_abstraction_for_self_suply_total_sw_nace_b + wa_abstraction_for_self_suply_total_sw_nace_c + wa_abstraction_for_self_suply_total_sw_nace_d + wa_abstraction_for_self_suply_total_sw_nace_i + wa_abstraction_for_self_suply_total_sw_other = wa_abstraction_for_self_suply_total_sw_total | error | Total freshwater abstraction from surface water for self supply must equal to the sum of the sectoral abstraction from surface water for self-supply. |
| WA011 | wa_abstraction_for_self_suply_total_sw_nace_a >= wa_abstraction_for_self_suply_total_sw_nace_a_irrgation | error | Abstraction from surface water for self supply for NACE A must be more than Abstraction from surface water for self supply for NACE A irrigation. |
| WA012 | wa_abstraction_for_self_suply_total_sw_nace_c >= wa_abstraction_for_self_suply_total_sw_nace_c_cooling | error | Abstraction from surface water for self supply for NACE C must be more than Abstraction from surface water for self supply for NACE C cooling. |
| WA013 | wa_abstraction_for_self_suply_total_sw_nace_d >= wa_abstraction_for_self_suply_total_sw_nace_d_cooling | error | Abstraction from surface water for self supply for NACE D must be more than Abstraction from surface water for self supply for NACE D cooling. |
| WA014 | wa_abstraction_for_self_suply_total_gw_domestic + wa_abstraction_for_self_suply_total_gw_nace_a + wa_abstraction_for_self_suply_total_gw_nace_b + wa_abstraction_for_self_suply_total_gw_nace_c + wa_abstraction_for_self_suply_total_gw_nace_d + wa_abstraction_for_self_suply_total_gw_nace_i + wa_abstraction_for_self_suply_total_gw_other = wa_abstraction_for_self_suply_total_gw_total | error | Total freshwater abstraction from groundwater for self supply must equal to the sum of the sectoral abstraction from groundwater for self-supply. |
| WA015 | wa_abstraction_for_self_suply_total_gw_nace_a >= wa_abstraction_for_self_suply_total_gw_nace_a_irrgation | error | Abstraction from groundwater for self supply for NACE A must be more than Abstraction from groundwater for self supply for NACE A irrigation. |
| WA016 | wa_abstraction_for_self_suply_total_gw_nace_c >= wa_abstraction_for_self_suply_total_gw_nace_c_cooling | error | Abstraction from groundwater for self supply for NACE C must be more than Abstraction from groundwater for self supply for NACE C cooling. |
| WA017 | wa_abstraction_for_self_suply_total_gw_nace_d >= wa_abstraction_for_self_suply_total_gw_nace_d_cooling | error | Abstraction from groundwater for self supply for NACE D must be more than Abstraction from groundwater for self supply for NACE D cooling. |
| WA018 | wa_abstraction_for_self_suply_total_sw_total + wa_abstraction_for_self_suply_total_gw_total = wa_abstraction_for_self_suply_total | error | Will be checked after the submission of the data. Not implemented in the WQ reporting tool. |
| WA019 | wa_available_groundwater ≥ wa_total_abstraction_gw | error | Available groundwater must be more than Total freshwater abstraction from groundwater |
| WA020 | wa_total_abstraction_gw + wb_water_imports + wb_bottled_imports + wb_reused_water_total + wb_desalinated_water_total >= wu_total_freshwater_used_total | warning | Will be checked after the submission of the data. Not implemented in the WQ reporting tool. |
|  | Regional Water Use |  |  |
| WU001 | wu_total_freshwater_used_domestic + wu_total_freshwater_used_nace_a + wu_total_freshwater_used_nace_b + wu_total_freshwater_used_nace_c + wu_total_freshwater_used_nace_d + wu_total_freshwater_used_nace_i + wu_total_freshwater_used_other = wu_total_freshwater_used_total | error | Total freshwater used must equal to the sum of the sectoral freshwater used. |
| WU002 | wu_total_freshwater_used_nace_a >= wu_total_freshwater_used_nace_a_irrgation | error | Total freshwater used for NACE A must be more than Total freshwater used for NACE A irrigation. |
| WU003 | wu_total_freshwater_used_nace_d >= wu_total_freshwater_used_nace_d_cooling | error | Total freshwater used for NACE D must be more than Total freshwater used for NACE D cooling. |
| WU004 | wu_total_freshwater_used_nace_c_food_ind + wu_total_freshwater_used_nace_c_basic_metals + wu_total_freshwater_used_nace_c_transport + wu_total_freshwater_used_nace_c_textiles + wu_total_freshwater_used_nace_c_paper + wu_total_freshwater_used_nace_c_chemicals + wu_total_freshwater_used_nace_c_other_manufact_ind <= wu_total_freshwater_used_nace_c | error | Total freshwater used for NACE C must be more than the sum of the freshwater used for all the subcategories of the NACE C. |
| WU005 | wu_total_freshwater_used_nace_c >= wu_total_freshwater_used_nace_c_cooling | error | Total freshwater used for NACE C must be more than Total freshwater used for NACE C cooling. |
| WU006 | wu_public_water_supply_domestic + wu_public_water_supply_nace_a + wu_public_water_supply_nace_b + wu_public_water_supply_nace_c + wu_public_water_supply_nace_d + wu_public_water_supply_nace_i + wu_public_water_supply_other = wu_public_water_supply_total | error | Total freshwater used from public water supply must equal to the sum of the sectoral freshwater used from public water supply. |
| WU007 | wu_public_water_supply_nace_a >= wu_public_water_supply_nace_a_irrgation | error | Freshwater used from public water supply for NACE A must be more than Freshwater used from public water supply for NACE A irrigation. |
| WU008 | wu_public_water_supply_nace_d >= wu_public_water_supply_nace_d_cooling | error | Freshwater used from public water supply for NACE D must be more than Freshwater used from public water supply for NACE D cooling. |
| WU009 | wu_public_water_supply_nace_c_food_ind + wu_public_water_supply_nace_c_basic_metals + wu_public_water_supply_nace_c_transport + wu_public_water_supply_nace_c_textiles + wu_public_water_supply_nace_c_paper + wu_public_water_supply_nace_c_chemicals + wu_public_water_supply_nace_c_other_manufact_ind <= wu_public_water_supply_nace_c | error | Freshwater used from public water supply for NACE C must be more than the sum of the freshwater used for all the subcategories of the NACE C. |
| WU010 | wu_public_water_supply_nace_c >= wu_public_water_supply_nace_c_cooling | error | Freshwater used from public water supply for NACE C must be more than Freshwater used from public water supply for NACE C cooling. |
| WU011 | wu_self_supply_domestic + wu_self_supply_nace_a + wu_self_supply_nace_b + wu_self_supply_nace_c + wu_self_supply_nace_d + wu_self_supply_nace_i + wu_self_supply_other = wu_self_supply_total | error | Total freshwater used from self-supply must equal to the sum of the sectoral freshwater used from self-supply. |
| WU012 | wu_self_supply_nace_a >= wu_self_supply_nace_a_irrgation | error | Freshwater used from self-supply for NACE A must be more than Freshwater used from self-supply for NACE A irrigation. |
| WU013 | wu_self_supply_nace_d >= wu_self_supply_nace_d_cooling | error | Freshwater used from self-supply for NACE D must be more than Freshwater used from self-supply for NACE D cooling. |
| WU014 | wu_self_supply_nace_c_food_ind + wu_self_supply_nace_c_basic_metals + wu_self_supply_nace_c_transport + wu_self_supply_nace_c_textiles + wu_self_supply_nace_c_paper + wu_self_supply_nace_c_chemicals + wu_self_supply_nace_c_other_manufact_ind <= wu_self_supply_nace_c | error | Freshwater used from self-supply for NACE C must be more than the sum of the freshwater used for all the subcategories of the NACE C. |
| WU015 | wu_self_supply_nace_c >= wu_self_supply_nace_c_cooling | error | Freshwater used from self-supply for NACE C must be more than Freshwater used from self-supply for NACE C cooling. |
| WU016 | wu_recycled_water_domestic + wu_recycled_water_nace_a + wu_recycled_water_nace_b + wu_recycled_water_nace_c + wu_recycled_water_nace_d + wu_recycled_water_nace_i + wu_recycled_water_other = wu_recycled_water_total | error | Total recycled water used must equal to the sum of the sectoral recycled water used. |
| WU017 | wu_recycled_water_nace_a >= wu_recycled_water_nace_a_irrgation | error | Recycled water used for NACE A must be more than Recycled water used for NACE A irrigation. |
| WU018 | wu_recycled_water_nace_d >= wu_recycled_water_nace_d_cooling | error | Recycled water used for NACE D must be more than Recycled water used for NACE D cooling. |
| WU019 | wu_recycled_water_nace_c >= wu_recycled_water_nace_c_cooling | error | Recycled water used for NACE C must be more than Recycled water used for NACE C cooling. |
| WU020 | wu_public_water_supply_total + wu_self_supply_total = wu_total_freshwater_used_total | error | Will be checked after the submission of the data. Not implemented in the WQ reporting tool. |

# Outlier rules in hydrological time series

## Extreme value checks

| Function | Rule definition | Description |
| --- | --- | --- |
| lower_limit(l) | l ≤ xi | All values xi must be greater than or equal a given lower limit l |
| upper_limit(u) | xi ≤ u | All values xi must be smaller than or equal a given upper limit u |
| upper_limit_area(u) | xi / Ax ≤ u | All values xi per area Ax of the region to which the time series refers, must be smaller than or equal a given upper limit u. The rule can be applied only to time series which refer to geographical areas with known extent. |
| limit_stdev(k,λ) | μ - λσ ≤ xi ≤ μ + λσ | All values should satisfy the given inequality, where μ is the mean value, σ the standard deviation and λ a given coefficient. The rule applies only to time series which are sufficiently long (≥ k values) |

## Temporal consistency checks

| Function | Rule definition | Description |
| --- | --- | --- |
| tc1(e1) | e1 > ¦xi -xi+1¦ | The absolute value of the difference between two subsequent values must remain below a given limit e1. |
| tc2(e2,k) | (i xi>k, xi+1>0: e2 > ¦xi - xi+1¦ / max(xi, xi+1) | This rule calculates the absolute value of the difference between two subsequent values of the time series over the maximum of the two values. The resulting value must be smaller than a given limit (e2). This way, unlike rule tc1, which compares absolute numbers, rule tc2 checks for specific patterns in time series and has therefore a broader application. The function (ratio) results to values between 0 and 1. Time series values lower than a given number k are ignored. The rule is most useful to validate time series expected to have low variability. In the contrary, the rule has little usage to time series, which are expected to show steep increase/decrease of values (e.g. hourly streamflow). In general, aggregated time series obey to smaller values for e2 than the same observations in disaggregated form. Similarly time series with coarse time step tend to obey to smaller e2 values than refined time steps of the same parameter. |
| tc3(k,l,λ) | (i (j i+k<j ≤i+l and k<l: xj ≤ λ⋅xi | A peak in the time series must be reduced to a lower level within a specified time period. This rule applies mainly to discharge or rainfall time series with a daily or smaller time step. k is an integer representing a number of values after the i-th value. Special case for precipitation: The value must return to zero within a specified period of time steps. Very small values are replaced by a minimum value. |