# Short GIS guidance for reporting under the Urban Waste Water Treatment Directive,  Appendix 1

# Data Dictionary

# Data Dictionary

According to the WFD CIS Guidance Document the aim of a Data Dictionary is to provide a common understanding of the file / table structure that should be used for the report of both tabular data and geographic datasets to the Commission.

# Note: Further developments of WISE-GIS guidance have to be considered here.

The recommended file names and geometry of the UWWTD tabular data and geographic data are listed in the Table 1 below.

# Table 1

| UWWTD datasets | Recommended File Name | Geometry Type |
| --- | --- | --- |
| Agglomeration | MS*_Agglo | point/table |
| UWWTP | MS*_UWWTP | Point/table |
| Discharge Point | MS*_DisPoint | Point/table |
| Sensitive Area - river | MS*_SA_river | Line/shape |
| Sensitive Area - lake | MS*_SA_lake | Polygon/shape |
| Sensitive Area – coastline | MS*_SA_coastl | Line/shape |
| Sensitive Area – coast area | MS*_SA_coasta | Polygon/shape |
| Sensitive Area – transitional water | MS*_SA_TW | Polygon/shape |
| Sensitive Area - catchment | MS*_SA_catchm | Polygon/shape |
| Less sensitive Area – transitional water | MS*_LSA_TW | Polygon/shape |
| Less sensitive area - coastline | MS*_LSA_coastl | Line/shape |

*MS = 2 character Member State identifier (for example UK_SA_river = Sensitive area river of United Kingdom)

The recommended attributes for each UWWTD geographic shape file are described in Tables 2 to 7. For each attribute a field name (shortened due to physical restriction on field name length e.g. dbase – 10 character), a text description, a generic field type and length, together with any restrictions (whether mandatory or optional) are provided.

Remark: The tables for point information (agglomeration, UWWTPs and Discharge Points) are covered by the electronic UWWTD-Questionnaire 2007 and therefore, not further explained in this document.

Table 2: MS*_SA_river

| MS*_SA_river |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (line) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| MemberStateSARiverCode | MSCD_SA_RV | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| EuropeanSARiverCode | EUCD_SA_RV | Unique code for Receiving area at EU level | ISO3166 & MSCD _SA_RV | String | 24 | Mandatory**, as per coding guidelines |
| Length | LENGTHKM | Total length of the River |  | Double | 9,2 | Optional** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

Table 3: MS*_SA_lake

| MS*_SA_lake |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (polygon) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanSALakeCode | EUCD_SA_LK | Unique code for Receiving area at EU level | ISO3166 & MSCD_SA_LK | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateSALakeCode | MSCD_SA_LK | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| AreaKM2 | AREAKM2 | Area in square kilometers |  | Double | 9,2 | Optional** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

# Table 4: MS*_SA_coastl

| MS*_SA_coastl |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (line) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanSACoastlineCode | EUCD_SA_CL | Unique code for Receiving area at EU level | ISO3166 & MSCD_SA_CO | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateSACoastlineCode | MSCD_SA_CL | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| Length | LENGTHKM | Total length of the coastline |  | Double | 9,2 | Optional** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

# Table 5: MS*_SA_coasta

| MS*_SA_coasta |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (polygon) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanSACoastareaCode | EUCD_SA_CA | Unique code for Receiving area at EU level | ISO3166 & MSCD_SA_CA | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateSACoastareaCode | MSCD_SA_CA | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| AreaKM2 | AREAKM2 | Area in square kilometers |  | Double | 9,2 | Mandatory** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

# Table 6: MS*_SA_TW

| MS*_SA_TW |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (polygon) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanSATransitionalwater Code | EUCD_SA_TW | Unique code for Receiving area at EU level | ISO3166 & MSCD_SA_TW | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateEuropeanSA TransitionalwaterCode | MSCD_SA_TW | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| AreaKM2 | AREAKM2 | Area in square kilometers |  | Double | 9,2 | Mandatory** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

# Table 7: MS*_SA_catchm

| MS*_SA_catchm |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (polygon) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanSACatchmentCode | EUCD_SA_CM | Unique code for Receiving area at EU level | ISO3166 & MSCD_SA_CM | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateSACatchmentCode | MSCD_SA_CM | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| AreaKM2 | AREAKM2 | Area in square kilometers |  | Double | 9,2 | Mandatory** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

# Table 8: MS*_LSA_TW

| MS*_LSA_TW |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (polygon) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanLSATransitionalwater Code | EUCD_LSATW | Unique code for Receiving area at EU level | ISO3166 & MSCD_LSATW | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateLSATransitional waterCode | MSCD_LSATW | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory* as per coding guidelines |
| AreaKM2 | AREAKM2 | Area in square kilometers |  | Double | 9,2 | Mandatory** |

**'mandatory' and 'optional' in technical terms in sense of GIS data

# Table 9: MS*_LSA_coastl

| MS*_LSA_coastl |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Attribute | FieldName | Definition | Values | Type | Length | Restrictions |
| shape | SHAPE |  |  | Geometry (line) |  |  |
| Name | NAME | Locally used name |  | String | 100 | Mandatory** |
| EuropeanLSACoastlineCode | EUCD_LSACL | Unique code for Receiving area at EU level | ISO3166 & MSCD_LSACL | String | 24 | Mandatory**, as per coding guidelines |
| MemberStateLSACoastlineCode | MSCD_LSACL | Unique code for Receiving area at Member State level |  | String | 22 | Mandatory**, as per coding guidelines |
| AreaKM2 | AREAKM2 | Area in square kilometers |  | Double | 9,2 | Mandatory** |

**'mandatory' and 'optional' in technical terms in sense of GIS data